## Slide 1: Chapter 5 Data-driven Prognostics

## Slide 2: 1. Introduction to Data-driven Prognostics

## Slide 3: Challenges in Physics-based Prognostics
physics-based prognostics approaches are a powerful tool for predicting the future behavior of damage degradation with a relatively small number of observed data
  They are limited to the case when a physical model that describes the damage degradation behavior is available
  the measured data must be directly related to the physical model
Physics-based prognostics may anticipate challenges when predicting failure of a complex system without well-defined physical model to describe degradation and when direct measurement of damage is impossible

## Slide 4: Ex) Bearing Spall
spall phenomenon where the rolling elements or race surface is damaged due to surface cracks
  An initial small surface crack quickly propagates into other regions of surface and gradually increases vibration of the shaft and system
  The excessive vibration eventually leads to the system failure
For SHM, these surface cracks cannot be measured directly while the bearing is rotating
  accelerometers are often installed in the stationary parts of the system to monitor the level of vibration
  the damage degradation is measured indirectly through the level of vibration
  there is no clear physical relationship between the degradation level and vibration level
Maintenance decision is made by the vibration level based on experience
  Reliable decision requires many run-to-fail data of similar systems

## Slide 5: Data-driven Prognostics
Data-driven approaches use information from observed data to identify the patterns of degradation progress and predict the future state without using a physical model
  still use some sort of mathematical model that works only for a particular system under monitoring
  can be considered as an extrapolation (prediction) method based on mathematical functions (degradation progress)
Training data
  several sets of degradation data up to the end of life as well as the data from the current system are required to identify the degradation characteristics
  used to make mathematical models learn the degradation behavior without a physical model
data-driven approaches are practical since physical degradation models are rare in practice

## Slide 6: Review of Data-Driven Approaches
A mathematical model output is a function of input variables and parameters
the mathematical model form must be determined first
Model parameters are identified using training data via optimization
  data are obtained under various usage conditions or at previous times under a given usage condition
  many sets of training data are required to prevent overfitting
Future degradation state is predicted based on the identified parameters and the mathematical model

## Slide 7: Data-Driven Prognostic Algorithms
Artificial intelligence approaches that include neural network (NN)
  NN has been used in wide fields and applications, such as time series prediction, classification/pattern recognition and robotics/control
  the most common algorithm used for prognostics
Statistical approaches including the Gaussian process (GP) regression
We will discuss GP and NN in this chapter

## Slide 8: Data-Driven Prognostics Using Gaussian Process (GP) Regression

## Slide 9: Surrogate Model and Extrapolation
Data-driven approaches fit the data using a mathematical function
fitting data with a mathematical function is referred to as a surrogate model
  In the fitting process, accuracy is uttermost important criterion
  If more data are available and if the surrogate model is flexible enough to follow all data, then an accurate surrogate model can be obtained
  Once fitted, evaluating function values at different input values are extremely cheap
The main purpose is to reduce the computational time for numerous calculation of the quantity of interest (degradation) at different input values (time)
  Surrogate modeling is popular in various engineering fields, such as engineering design and reliability assessment

## Slide 10: Surrogate Model for Prognostics
In prognostics, the surrogate model is used for a different purpose
  time is often used as an input variable (to predict the RUL of a system)
  the main purpose of surrogate is not reducing computational time, but accurate prediction in the future time
  Most applications usually predict the quantity of interest within the range of input data (interpolation )
In prognostics, it is to predict the degradation level in future time (extrapolation)
  If degradation levels are measured up to the current time, they are used to fit a surrogate model to predict the degradation level in future time
a surrogate behaves quite different between interpolation and extrapolation region
  A surrogate model with a good fit in interpolation region can miserably fail in predicting in the extrapolation region

## Slide 11: Interpolation vs. Extrapolation in Surrogate
Approximate using 21 equally-spaced samples in the range of [1, 9]
Fit the 21 samples using newrb (Matlab) radial-basis neural network in the range of [0, 10]
Surrogate fits are extremely accurate in [1, 9], but miserably failed in [0, 1] and [9, 10]
x=linspace(1,9,21); y=x+0.5*sin(5*x);
net=newrb(x,y);
xf=linspace(0,10,101); yf=xf+0.5*sin(5*xf);
ysim=sim(net,xf);
plot(xf,yf); hold on; plot(xf,ysim,'ro')

## Slide 12: Surrogate for Extrapolation
it is important to evaluate surrogates for the perspective of extrapolation in prognostics
RBNN may not be a good surrogate as it does not carry the trend of degradation
Polynomial response surface may follow the trend relatively well, but it tends to change the curvature quickly in the extrapolation region
Gaussian process (GP) regression surrogate model turns out to be most robust in terms of extrapolation
In the surrogate community, GP is often called Kriging surrogate

## Slide 13: Introduction to Kriging
Method invented in the 1950s by South African geologist Daniel G. Krige (1919-2013) for predicting distribution of minerals.
  Formalized by French engineer, Georges Matheron in 1960.
  Statisticians refer to a more general Gaussian Process regression.
Became very popular for fitting surrogates to expensive computer simulations in the 21st century.
It is one of the best surrogates available.
It probably became popular late mostly because of the high computer cost of fitting it to data.
Notes: Kriging was invented in the 1950s by Daniel Krige (Professor at University of the Witwatersrand, Republic of South Africa), a South African geologist , for the purpose of predicting the distribution of minerals on the basis of samples. It became very popular for fitting surrogates to expensive computer simulations only about 40-50 years later. This is at least partly because it is an expensive surrogate in terms of computation, and it had to wait until computers became fast enough.
My experience is that of all currently popular surrogates, it has the highest chance of being the most accurate for a given problem. However, from my experience that chance is still less than 50%.
Krige, D. G. (1951). "A statistical approach to some basic mine valuation problems on the Witwatersrand". J. of the Chem., Metal. and Mining Soc. of South Africa 52 (6): 119–139.
Matheron, G., "Principles of geostatistics", Economic Geology, 58, pp 1246–1266, 1963

## Slide 14: Kriging philosophy
We assume that the data is sampled from an unknown function that obeys simple correlation rules.
The value of the function at a point is correlated to the values at neighboring points based on their separation in different directions.
The correlation is strong to nearby points and weak with far away points, but strength does not change based on location, only separation between points.
Normally Kriging is used for noise free data so that it interpolates exactly the function values.
Notes: For linear regression we normally assume that we know the functional shape (e.g. a polynomial) and the data is to be used to find the coefficients that will minimize the root mean square errors at the data points. Kriging takes a very different approach. It assumes that we don’t know much about the function, except for the form of correlation between the value of the function at nearby points. In particular, the correlation depends only on the separation between points and decays as they are further apart.
Kriging is a smooth predictor. If two points are close, then their Kriging estimates are close.
Kriging is usually used as an interpolator, so that if fits exactly the data, and we could not use the rms error as a way to find its parameters. That is, we assume that there is no noise in the data. There is a version of kriging with noise (often called kriging with a nugget).
Because of the correlation decay, kriging is a local surrogate with shape functions that are similar to those used for radial basis surrogates, except that the decay can be different in different directions.

## Slide 15: Reminder: Covariance and Correlation
Covariance of two random variables X and Y
The covariance of a random variable with itself is the square of the standard deviation
Covariance matrix
Correlation
The correlation matrix has 1 on the diagonal.
Notes: This is a reminder of the basic statistical quantities of covariance of pair of random variables and the important concept of correlation. Remember that the variance of a random variable, is the first moment around its mean, or the square of the standard deviation. The covariance of a pair of random variables is the mixed moment of the two variables.
Correlation measures their propensity to move together. So a correlation of 1 means that they increase and decrease in perfect synchrony. The most common case is when X=cY, where c is a positive constant.
Similarly a correlation of -1 also means perfect synchrony, but in the opposite direction, and X=cY, with c a negative constant is a common case. Finally, a correlation of 0 means that they are not related. The common case is when the random variables are independent, but not all uncorrelated variables are independent. Zero correlation relates to the first moment, but there may be dependence through higher order effects.
The correlation matrix is the matrix of correlation of the components of a vector. It has 1 on the diagonal, because each variable is perfectly correlated with itself.

## Slide 16: Correlation between functions at near and far points
Generate 10 random samples, translate them by a bit (0.1), and by more (1.0)
  x=10*rand(1,10);
  xnear=x+0.1; xfar=x+1;
  ynear=sin(xnear);
  y=sin(x);
  yfar=sin(xfar);
Compare corelations:
  r=corrcoef(y,ynear) 0.9894; High correlation
  rfar=corrcoef(y,yfar) 0.4229; Low correlation
Decay to about 0.4 over one sixth of the wavelength.
  Wavelength on sine function is 2~6
Notes: The fitting process in kriging needs to estimate how fast the correlation between function values decays with distance. This depends on the wavelength of the function, with short wavelength corresponding to fast decay. In the example here, we check how fast the correlation decays for sin(x) that has a wave length of 2p.
To illustrate the values of correlations that are expected between function values, we generate random numbers between 0 and 10 and evaluate the sine function at these points. We also translate the points by a small amount compared to the wavelength (0.1) and a larger amount (1.0) and calculate the correlation coefficients between the function values in the original and translated sets.
The correlation coefficient is about 0.99 with the nearby points and 0.42 with the set further away. This reflects the change in function values, as illustrated by the pair of points marked in red.
In kriging, finding the rate of correlation decay is part of the fitting process. This example shows us that with a wavy function we can expect the correlation to decay to about 0.4 over one sixth of the wavelength.

## Slide 17: Universal Kriging approximation
Kriging is similar to PRS, but starting from statistical view
Ex) Linear global function
Measurement data
  Predictions are exact at data points
Local departure
(random process)
Trend function
Global function
(low-order polynomials)
x
z, y
Mean of Kriging prediction
Sampling data points
Systematic Departure
Trend Model

## Slide 18: Universal Kriging Approximation cont.
Local departure
  The difference between the prediction and global trend function
  Kriging assumes that follows a Gaussian process
  : standard deviation of data w.r.t. the global function

## Slide 19: Ordinary and simple Kriging
Ordinary Kriging: constant trend function
Simple Kriging: constant trend function is known (often 0)
Assumption: Systematic departures are correlated.
Kriging prediction comes with a normal distribution of the uncertainty in the prediction
At the sample points, the uncertainty is zero
Notes: The most general version of kriging is called universal kriging, and it includes a linear trend function and the deviation which includes the local contributions and is governed by the correlation function.
The trend function is composed of known shape functions and coefficients to be determined. The shape functions are typically monomials, so that popular trend functions are linear and quadratic polynomials.
Here we will limit the description to a constant trend, a version of kriging known as ordinary kriging, with the constant estimated from the data. Another version of kriging, known as simple kriging is when the constant is assumed to be known.
As in linear regression, the kriging fit, shown in red in the figure, is only the mean of a normal distribution, and the distribution can be used to provide estimates of uncertainty in the kriging predictions, as well as guide the placements of further sampling points so as to reduce the uncertainty in the kriging prediction.
Caution: Note that the figure is misleading in that the uncertainty at the points where the data is given is zero when there is no noise. The uncertainty is larger in between data points.
The most general version of kriging is called universal kriging, and it includes a linear trend function and the deviation ├ 𝑍(𝐱)which includes the local contributions and is governed by the correlation function.
𝑦 ̂(𝐱)=∑129_(𝑖=1)^(𝑁_𝑣)▒├ 𝛽_𝑖 𝜉_𝑖 (𝐱) +𝑍(𝐱)
The trend function is composed of known shape functions 𝜉_𝑖 (𝐱) and coefficients 𝛽_𝑖 to be determined. The shape functions are typically monomials, so that popular trend functions are linear and quadratic polynomials.
Here we will limit the description to a constant trend, a version of kriging known as ordinary kriging, with the constant estimated from the data. Another version of kriging, known as simple kriging is when the constant is assumed to be known.
As in linear regression, the kriging fit, shown in red in the figure, is only the mean of a normal distribution, and the distribution can be used to provide estimates of uncertainty in the kriging predictions, as well as guide the placements of further sampling points so as to reduce the uncertainty in the kriging prediction.
Caution: Note that the figure is misleading in that the uncertainty at the points where the data is given is zero when there is no noise. The uncertainty is larger in between data points.

## Slide 20: Correlation model
Kriging assumes that predictions are correlated inversely proportional to the distance
Systematic departure captures this correlation
  Zero mean:
  Covariance of data:
  Variance of function:
  Isotropic correlation:
  Anisotropic correlation:

## Slide 21: Isotropic vs. anisotropic correlation functions
(a) Isotropic correlation
(b) Anisotropic correlation

## Slide 22: Gaussian correlation function
Correlation between point and point
: hyperparameter, decaying rate
The correlation should decay to about 0.4 at one sixth of the wavelength and
Approximately
For the function we would like to estimate
Notes: The most popular correlation decay function for kriging is Gaussian. Given two points x (with components ) and s we assume that the correlation of the unknown function Z at these two points is given as
Where the larger is, the faster the decay of the correlation with distance. For =1, the decay in the ith direction is 1/e=0.37, which approximately corresponds to what we found for one sixth of the wavelength for the function sin(x). So if the wavelength in the ith direction is , we should have approximately
So for the function we have ~(6/5) so we should use .
The gaussian correlation function can also be generally referred to as gaussian kernel or basis functions.
The most popular correlation decay function for kriging is Gaussian. Given two points x (with components 𝑥_𝑖) and s we assume that the correlation of the unknown function Z at these two points is given as
𝐶(𝑍(𝐱),𝑍(𝐬),𝛉)=∏129_(𝑖=1)^(𝑁_𝑣)▒exp(−𝜃_𝑖 (𝑥_𝑖−𝑠_𝑖 )^2 )
Where the larger 𝜃_𝑖 is, the faster the decay of the correlation with distance. For 𝜃_𝑖=1, the decay in the ith direction is 1/e=0.37, which approximately corresponds to what we found for one sixth of the wavelength for the function sin(x). So if the wavelength in the ith direction is 𝑙_𝑖, we should have approximately
𝜃_𝑖 (𝑙_𝑖∕6)^2=1" or" 〖 𝜃〗_𝑖=36∕𝑙_𝑖^2
So for the function ├ 𝑦=sin(𝑥_1)∗sin(5𝑥_2 ) we have 𝑙_1≈6," " 𝑙_2≈1.2 so we should use 𝜃_1≈1," " 𝜃_2≈25.

## Slide 23: Notation
sample points , with -dimension of input and
Given decay rates , the covariance matrix of the data
The correlation matrix R is formed from the covariance matrix, assuming a constant standard deviation which measures the uncertainty in function values (stationary covariance)
Small for dense data, large for sparse data
  How do you decide whether the data is sparse or dense?
Notes: We use subscripts to denote components of a vector, and superscript to identify data points. We are in n dimensional space, and we have data points.
In the process of fitting the data, we will also need to estimate the decay rates and the standard deviation . The standard deviation will be small when the data is dense. Dense means that we have more than enough points to describe the waviness of the function. That means that the distance from one point to the nearest one should be an order of magnitude less than the wavelength of the function.
We use subscripts to denote components of a vector, and superscript to identify data points. We are in n dimensional space, and we have 𝑛_𝑦 data points.
In the process of fitting the data, we will also need to estimate the decay rates 𝜃_𝑘 and the standard deviation 𝜎. The standard deviation will be small when the data is dense. Dense means that we have more than enough points to describe the waviness of the function. That means that the distance from one point to the nearest one should be an order of magnitude less than the wavelength of the function..

## Slide 24: Kriging vs. PRS
Kriging PRS
PRS assumes that is a correct form, but data have error that are statistically independent
Kriging assumes that data are accurate, but the model form is uncertain  Kriging fits data
At prediction points, error in Kriging is described by local departure

## Slide 25: GP Simulation
GP simulation function is derived using measured data
  Need to determine global function parameters, , and the variance of data w.r.t. global function, using MLE
  Local departure is calculated by minimizing the unbiased mean-squares-error
Error b/w data and global function

## Slide 26: Determining the global function
Assumption: error and correlation between data
Maximum likelihood estimate (MSE)
  Likelihood: PDF of getting data for given parameters, and
  Use joint PDF of correlated data to define likelihood
  This is multiplication of Gaussian distributions
  : correlation matrix, : determinant of correlation matrix
Parameters, and , can be found by maximizing the likelihood function

## Slide 27: Maximum likelihood estimate (MLE)
Logarithmic likelihood (ignore for now)
Stationary condition
Solve for and
PRS linear regression
For unbiased estimate

## Slide 28: Maximum likelihood estimate (MLE)
Estimate parameter is similar to linear regression, except for having
For the unbiased estimation, is used instead of
Estimated parameters, , depends on correlation
It is assumed that covariance matrix is constant
  the wavelength of the function is uniform in all regions of input space
Ordinary and simple Kriging is not a good choice for prognostics
  purpose of prognostics is for extrapolation where the correlation is quickly diminished as the extrapolation distance increases and the prediction goes back to the global function

## Slide 29: Local departure
Kriging passes data point  Kriging can be expressed by a linear combination of data and weights:
Minimizing mean squared error (MSE)
No error in data:
  : local departure function
  : local departure vector at data points
True function:
Weight function

## Slide 30: Error term
Goal: to determine the weight function that minimizes the error
Even if the GP simulation is shown in the form of , this form will be expressed in terms of the global function and local departure
Error:
Global error
Departure error

## Slide 31: Minimize MSE
To keep the global function unbiased, a constraint of global error being zero is added
MSE is the variance (uncertainty) in Kriging prediction
Goal: find that minimizes MSE while satisfying the unbiased constraint

## Slide 32: Lagrange function for constrained optimization
Lagrange function (min. MSE with constraint)
Stationary conditions (KKT)
Lagrange multiplier

## Slide 33: Kriging prediction
Kriging as linear combination of data and weight functions
  Local departure term is the weighted sum of the trend function error based on the correlation term
Global function
Local departure

## Slide 34: Simplification for ordinary Kriging
For ordinary Kriging, and (mean of data)
Linear in that the radial basis can be viewed as basis functions
The prediction is linear in the data y, in common with linear regression, but b is not calculated by minimizing MSE.
  the basis function, , is unknown, in that the correlation matrix, , needs to be estimated from the data
Note that far away from data, (not good for substantial extrapolation)
Notes: The form of the surrogate for ordinary kriging is
Where is the constant, the estimated mean value. The vector b of coefficient is , and the shape functions that it multiplies are the exponentials
So kriging is similar to linear regression, which is a linear combination of unknown coefficients time known shape function. However, there are two important differences. First the shape functions are not known, in that the decay rates will be estimated from the data (in the next slide). Second, the coefficients are not found by minimizing the rms error at the data points (which is zero, because the data is exactly interpolated).
Note that since the exponentials decay away from the data points, when we are far from all data points the prediction will be close to . So ordinary kriging is not good for substantial extrapolation. If we expect to need to extrapolate far from data points, we should use universal kriging with a trend.
The form of the surrogate for ordinary kriging is
𝑦 ̂(𝐱)=𝜇 ̂+𝐫^𝑇 𝑅^(−1) 𝐲=𝜇 ̂+𝐛^𝑇 𝐫
Where 𝜇 ̂ is the constant, the estimated mean value. The vector b of coefficient is 〖𝒃=𝑅〗^(−1) 𝐲, and the shape functions that it multiplies are the exponentials
𝑟_𝑖=exp(−∑129_(𝑘=1)^𝑛▒〖𝜃_𝑘 (𝑥_𝑘^((𝑖) )−𝑥_𝑘^ )^2 〗)
So kriging is similar to linear regression, which is a linear combination of unknown coefficients time known shape function. However, there are two important differences. First the shape functions are not known, in that the decay rates 𝜃_𝑘 will be estimated from the data (in the next slide). Second, the coefficients are not found by minimizing the rms error at the data points (which is zero, because the data is exactly interpolated).
Note that since the exponentials decay away from the data points, when we are far from all data points the prediction will be close to 𝜇 ̂ . So ordinary kriging is not good for substantial extrapolation. If we expect to need to extrapolate far from data points, we should use universal kriging with a trend.

## Slide 35: Correlation Function and Hyperparameters
Correlation functions
  radial basis (or squared exponential), rational quadratic, neural network, Matern, periodic, constant, linear functions
Commonly used one-parameter radial basis function
  depends on the distance between inputs, i.e., the Euclidean norm and : hyperparameter, decaying rate
  The correlation should decay to about 0.4 at one sixth of the wavelength and
  Approximately
  For ,

## Slide 36: Estimating hyperparameters
Estimating and depends on hyperparameter in R
Maximizing the log-likelihood that the data comes from a Gaussian process defined by .
Once is found, the estimate of the mean and standard deviation is obtained as (ordinary Kriging)
will be canceled with
Equivalent

## Slide 37: Difficulty in MLE
Maximum likelihood is a tough optimization problem
  the likelihood often varies slowly in a wide range of argument
  Some Kriging codes minimize the cross-validation error instead
Cross-validation estimation
  leaves out one of the points, fits the rest with the parameters, and calculates the error at the left-out point
  repeated for every point to produce a total error measure
  the set of parameters that yields the lowest cross-validation error is chosen
Optimization for parameters is often ill-conditioned
  lead to either a poor fit or poor estimate of the prediction variance

## Slide 38: Comparison b/w RMSE and MLE
Discontinuous
Good
MLEmin RMSE
More than 2 hyperparameters

## Slide 39: Kriging fitting issues
MLE or cross-validation optimization problem solved to obtain the kriging fit is often ill-conditioned leading to poor fit, or poor estimate of the prediction variance.
Poor estimate of the prediction variance can be checked by comparing it to the cross validation error.
Poor fits are often characterized by the kriging surrogate having large curvature near data points.
It is recommended to visualize by plotting the kriging fit and its standard error.

## Slide 40: Ex) Quadratic function fit
Use 9 data and a constant global function to fit a quadratic function
Covariance
Too large
Good fit with poor variance
Too small
Bad fit with poor variance
Notes: The example of fiting a quadratic function was used with several kriging packages, using the points shown in the figure or also additional points outside the range. The two cases shown on the next slide are extreme cases for this simple function, but they show the kind of behavior that is occasionally encountered and can be detected by plotting the kriging fit and bounds representing two standard errors.

## Slide 41: Ex) Kriging fit
Fit data , for the global function using ordinary Kriging with
  For ordinary Kriging, and
  y=[1 0.99 0.99 0.94 0.95]’; % measurement data
  x=[0 5 10 15 20]'; % input variable
  X=ones(5,1); % design matrix
  ny=length(y); np=size(X,2);
  Correlation matrix
  h=5.2;
  for k=1:ny; for l=1:ny;
  R(k,l)=exp(-(norm(x(k,:)-x(l,:))/h)^2);
  end; end;

## Slide 42: Ex) Kriging fit cont.
Global function parameters
  Rinv=inv(R);
  thetaH=(X'*Rinv*X)\(X'* Rinv*y);
  sigmaH=sqrt(1/(ny-np)*((y-X*thetaH)'*Rinv*(y-X*thetaH)));
Estimate the optimum hyperparameter
  Instead of optimization the hyperparameter, we calculate it graphically
  We used this value in calculating and

## Slide 43: Ex) Kriging fit cont.
Matlab code for the graph
Prediction at (this is a sample point)
  Exact at the sample point !
  h=zeros(20,1); Obj=zeros(20,1);
  for i=1:20
  h(i)=0.5*i;
  for k=1:ny; for l=1:ny;
  R(k,l)=exp(-(norm(x(k,:)-x(l,:))/h(i))^2);
  end; end;
  Rinv=inv(R);
  thetaH=(X'*Rinv*X)\(X'* Rinv*y);
  sigmaH=sqrt(1/(ny-np)*((y-X*thetaH)'*Rinv*(y-X*thetaH)));
  Obj(i)=log(sigmaH^(2*(ny-np))*det(R));
  end
  plot(h,Obj,'linewidth',2); grid on;

## Slide 44: Ex) Kriging fit cont.
Prediction at (prediction point)
  xNew=10; %or xNew=14
  for k=1:ny; r(k,1)=exp(-(norm(x(k,:)-xNew)/h)^2); end;
  gpDepar=r'*Rinv*(y-X*thetaH);

## Slide 45: Prediction Variance
Square root of variance is called standard error.
The uncertainty at any is normally distributed.
represents the mean of Kriging prediction.
Notes: Once we have fitted the kriging parameters, besides the surrogate estimate, , we also get a prediction variance or the variance of the estimate as
The square root of V is estimate of the standard deviation, called the standard error. It is often shown along the kriging fit by a shaded area as can be seen in the top right figure.
In general it is high far from data points and low near data points. It can be used to decide where to put additional data points in order to reduce the uncertainty in the kriging predictions (that is add points where V is maximal).
For some applications we take advantage that the distribution of uncertainty about the prediction is normal, with being the mean and the standard error being the standard deviation, as shown in the left figure. This entire distribution is used for the Efficient Global Optimization in order to find points that have maximal expected improvement over the best sample value available so far.
For derivations one can refer to: Sacks, J., Welch, W.J., Mitchell, T.J. and Wynn, H.P. (1989), Design and analysis of computer experiments (with discussion), Statistical Science 4: 409–435.
Once we have fitted the kriging parameters, besides the surrogate estimate, ├ 𝑦 ̂(𝐱), we also get a prediction variance or the variance of the estimate as
The square root of V is estimate of the standard deviation, called the standard error. It is often shown along the kriging fit by a shaded area as can be seen in the top right figure.
In general it is high far from data points and low near data points. It can be used to decide where to put additional data points in order to reduce the uncertainty in the kriging predictions (that is add points where V is maximal).
For some applications we take advantage that the distribution of uncertainty about the prediction is normal, with ├ 𝑦 ̂(𝐱) being the mean and the standard error being the standard deviation, as shown in the left figure. This entire distribution is used for the Efficient Global Optimization in order to find points that have maximal expected improvement over the best sample value available so far.
For derivations one can refer to: Sacks, J., Welch, W.J., Mitchell, T.J. and Wynn, H.P. (1989), Design and analysis of computer experiments (with discussion), Statistical Science 4: 409–435.
45

## Slide 46: Prediction uncertainty
Kriging prediction is the mean prediction and MSE is the variance
Kriging prediction is Gaussian distribution
  This is an estimated uncertainty using data
  When the # of data is small, use t-distribution
Ordinary Kriging

## Slide 47: Prediction Variance at Data Points
prediction variance is zero at data points
Let , at data point
  because is a unit vector whose th component is one
  is th row of
Therefore, Lagrange multiplier = 0
MSE
a unit vector whose th component is one

## Slide 48: Ex) Kriging fit cont.
90% confidence intervals at
  Standard error:
  xi=1;
  w=Rinv*r+Rinv*X*((X'*Rinv*X)\(xi'-X'*Rinv*r));
  zSigmaH=sigmaH*sqrt(w'*R*w-2*w'*r+1);
  % using the inverse calculation
  gpMean=0.9482; % from Example 5.2
  PI=[ gpMean + tinv(0.05,ny-np)*zSigmaH, ...
  gpMean + tinv(0.95,ny-np)*zSigmaH]
  % using the random samples
  ns=5e3;
  tDist=trnd(ny-np,1,ns);
  yHat=gpMean+tDist*zSigmaH;
  PI=prctile(yHat,[5 95])
xnew | 5 percentile | 95 percentile | 90% P.I.
x = 10 | 0.99 | 0.99 | 0
x = 14 | 0.9394 | 0.9570 | 0.0176

## Slide 49: Kriging with nuggets
Nuggets – refers to the inclusion of noise at data points.
The more general Gaussian Process surrogates or Kriging with nuggets can handle data with noise (e.g. experimental results with noise).

## Slide 50: GP: Matlab code for Gaussian Process
function rul=GP(funcOrd,h0)
clear global; global DegraUnit ...
TimeUnit time y thres signiLevel ns ny nt xTrain yTrain X dof
%=== PROBLEM DEFINITION 1 (Required Variables) ==============
WorkName=' '; % work results are saved by WorkName
DegraUnit=' '; % degradation unit
TimeUnit=' '; % time unit (Cycles, Weeks, etc.)
time=[ ]'; %[cv]: time at both measurement and prediction
y=[ ]'; %[ny x 1]: measured data
nT= ; % num. of training set including the current one
nt=[ ]';%[nT x 1]: num. of training data in each training set
thres= ; % threshold (critical value)
degraTrue=[ ]'; %[cv]: true values of degradation
signiLevel= ; % significance level for C.I. and P.I.
ns= ; % number of particles/samples
%=== PROBLEM DEFINITION (Training Matrix) ===================
xTrain=[ ]; yTrain=[ ];
%============================================================

## Slide 51: GP Matlab code cont.
% % % PROGNOSIS using GP
ny=length(y);
X=GLOBAL(xTrain,funcOrd); %% Determine Hyperparameter
dof=size(yTrain,1)-size(X,2);
hMax=2; hBound=hMax*ones(1,length(h0));
hH=fmincon(@FUNC,h0,[],[],[],[],-hBound,hBound);
[R,thetaH,sigmaH]=RTHESIG(hH); %% R, Theta, and Sigma
%=== PROBLEM DEFINITION 2 (Input Matrix for Prediction ======
for k=1:length(time(ny:end)); %% Degradation Prediction
xNew=[ ];
[zMean(k,:),zSig(k,:)]= ...
GPSIM(xNew,funcOrd,hH,R,thetaH,sigmaH);
end;
%============================================================
tDist=trnd(dof,size(zMean,1),ns); %% Prediction Uncertainty
zHat0=repmat(zMean,1,ns)+tDist.*repmat(zSig,1,ns);
zHat=zHat0*(max(y)-min(y))+min(y);
degraPredi=zHat;
% % % POST-PROCESSING
rul=POST([],degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);
end

## Slide 52: GP Matlab code cont.
% % % GLOBAL FUNCTION
function X=GLOBAL(x0,funcOrd)
nx=size(x0,1);
if funcOrd==0; X=ones(nx,1);
elseif funcOrd==1; X=[ones(nx,1) x0];
elseif funcOrd==2; X=[ones(nx,1) x0 x0.^2];
end
end
% % % OBJECTIVE FUNCTION TO FIND H
function objec=FUNC(h)
global dof
[R,~,sigma]=RTHESIG(h);
objec=log(sigma^(2*dof)*det(R));
end
% % % R, THETA, and SIGMA
function [R,theta,sigma]=RTHESIG(h)
global xTrain yTrain X dof
R=CORREL(xTrain,h); Rinv=R^-1;
theta=(X'*Rinv*X)\(X'*Rinv*yTrain);
sigma=sqrt(1/dof*((yTrain-X*theta)'*Rinv*(yTrain-X*theta)));
end

## Slide 53: GP Matlab code cont.
% % % CORRELATION FUNCTION
function R=CORREL(x0,h)
global xTrain
for k=1:size(xTrain,1); for l=1:size(x0,1);
R(k,l)=exp(-(norm(xTrain(k,:)-x0(l,:))/h)^2);
end; end;
end
% % % GP SIMULATION at NEW INPUTS
function [zMean,zSig]=GPSIM(x,funcOrd,h,R,theta,sigma)
global yTrain X
Rinv=R^-1;
xi=GLOBAL(x,funcOrd);
r=CORREL(x,h);
zMean=xi*theta+r'*Rinv*(yTrain-X*theta);
w=Rinv*r+Rinv*X*((X'*Rinv*X)\(xi'-X'*Rinv*r));
zSig=sigma*sqrt(w'*R*w-2*w'*r+1);
end

## Slide 54: GP Implementation of Battery Prognostics
Problem definition
  Mostly use the same convention of NLS, BM, and PF
Possible to have multiple sets of training data
  nT is the number of training sets including prediction set
  nt is a nT×1 vector of the number of training data in each data set
  Ex) nT = 3, nt = [20 20 10]’: Two sets of 20 run-to-fail data from similar systems and 10 data from the current system
True degradation is given in the form of data
time=[0:5:200]';
y=[1.00 0.99 0.99 0.94 0.95 0.94 0.91 0.91 0.87 0.86]';
nT=1;
nt=[10]';
degraTrue=exp(-0.003.*time);

## Slide 55: Problem Definition cont.
No physical model  Training data are uses instead
  Normalizing input and output data in [0, 1] is required to find the hyperparameter properly
Also, need normalization for prediction time
%=== PROBLEM DEFINITION (Training Matrix) =================
y0=(y-min(y))/(max(y)-min(y));
time0=(time-min(time))/(max(time)-min(time));
xTrain=time0(1:length(y)); yTrain=y0;
%============================================================
xNew=time0(ny-1+k);

## Slide 56: Global Function of GP
Global function
  User can choose constant, linear or quadratic global function using funcOrd = 0, 1, or 2.
  Global function basically calculates the design matrix
% % % GLOBAL FUNCTION
function X=GLOBAL(x0,funcOrd)
nx=size(x0,1);
if funcOrd==0; X=ones(nx,1);
elseif funcOrd==1; X=[ones(nx,1) x0];
elseif funcOrd==2; X=[ones(nx,1) x0 x0.^2];
end
end

## Slide 57: Optimization to Find Hyperparameter
We need a function that can calculate for given hyperparameter
Correlation function
% % % R, THETA, and SIGMA
function [R,theta,sigma]=RTHESIG(h)
global xTrain yTrain X dof
R=CORREL(xTrain,h); Rinv=R^-1;
theta=(X'*Rinv*X)\(X'*Rinv*yTrain);
sigma=sqrt(1/dof*((yTrain-X*theta)'*Rinv*(yTrain-X*theta)));
end
% % % CORRELATION FUNCTION
function R=CORREL(x0,h)
global xTrain
for k=1:size(xTrain,1); for l=1:size(x0,1);
R(k,l)=exp(-(norm(xTrain(k,:)-x0(l,:))/h)^2);
end; end;
end

## Slide 58: Calling GP
Negative log-likelihood (we will minimize this function)
Calling GP
  funcOrd = 1 (linear global function)
  : initial value of hyperparameter
% % % OBJECTIVE FUNCTION TO FIND H
function objec=FUNC(h)
global dof
[R,~,sigma]=RTHESIG(h);
objec=log(sigma^(2*dof)*det(R));
end
rul=GP(1,0.05);

## Slide 59: Prognosis using GP
Finding hyperparameter hH
  Starting from h0, find hH that minimizes the negative log-likelihood
  The range of hH is limited between [-2, 2]: to prevent ridiculously large value of the scale parameter
  Once hH is found, use it to calculate
Finding hyperparameter is equivalent to training the GP model
% % % PROGNOSIS using GP
ny=length(y);
X=GLOBAL(xTrain,funcOrd); %% Determine Hyperparameter
dof=size(yTrain,1)-size(X,2);
hMax=2; hBound=hMax*ones(1,length(h0));
hH=fmincon(@FUNC,h0,[],[],[],[],-hBound,hBound);
[R,thetaH,sigmaH]=RTHESIG(hH); %% R, Theta, and Sigma

## Slide 60: GP Simulation
Prediction using
  GP simulation calculates mean, zMean, and STD, zSig
% % % GP SIMULATION at NEW INPUTS
function [zMean,zSig]=GPSIM(x,funcOrd,h,R,theta,sigma)
global yTrain X
Rinv=R^-1;
xi=GLOBAL(x,funcOrd);
r=CORREL(x,h);
zMean=xi*theta+r'*Rinv*(yTrain-X*theta);
w=Rinv*r+Rinv*X*((X'*Rinv*X)\(xi'-X'*Rinv*r));
zSig=sigma*sqrt(w'*R*w-2*w'*r+1);
end
%=== PROBLEM DEFINITION 2 (Input Matrix for Prediction ======
for k=1:length(time(ny:end)); %% Degradation Prediction
xNew=time0(ny-1+k);
[zMean(k,:),zSig(k,:)]= ...
GPSIM(xNew,funcOrd,hH,R,thetaH,sigmaH);
end;
%============================================================

## Slide 61: Prediction Uncertainty and Postprocessing
Student’s t-distribution to generate samples of prediction
  Need to unscale
Postprocessing
  No model parameters for data-driven prognostics
tDist=trnd(dof,size(zMean,1),ns); %% Prediction Uncertainty
zHat0=repmat(zMean,1,ns)+tDist.*repmat(zSig,1,ns);
zHat=zHat0*(max(y)-min(y))+min(y);
degraPredi=zHat;
% % % POST-PROCESSING
rul=POST([],degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);

## Slide 62: Ex) Degradation and RUL of Battery Prognostics
Percentiles of RUL at 45 Cycles
5th: 39.5361, 50th (median): 49.9718, 95th: 58.7455.

## Slide 63: Neural Network Model

## Slide 64: Artificial neural network
Computing systems vaguely inspired by the biological neural networks that constitute animal brains
  The data structures and functionality of neural nets are designed to simulate associative memory
  Learn by processing input and output data (samples)
  After learn by enough data, neural nets can predict results from inputs
Relationship between the number and diversity of samples processed by a neural net and the prediction accuracy
Fancy description, but basically neural network is a kind of surrogate model
  Determine (train) unknown parameters using samples and predict

## Slide 65: Artificial neural network cont.
based on a collection of connected units or nodes called artificial neurons
  loosely model the neurons in a biological brain
  Each connection can transmit a signal to other neurons
  A neuron receives a signal then processes it and sends the signal to the neurons connected to it
Implementation
  "signal" at a connection is a real number, and the output of each neuron is computed by a nonlinear function of the sum of its inputs
  Neurons typically have a weight that adjusts as learning proceeds
  Input layer (inputs), hidden layer (not shown), and output layer (prediction)

## Slide 66: Deep learning
part of a broader family of machine learning methods based on artificial neural networks with representation learning
  Learning can be supervised, semi-supervised or unsupervised
The adjective "deep" comes from the use of multiple layers in the network
  Deep learning is a modern variation which is concerned with an unbounded number of layers of bounded size
  permits practical application and optimized implementation

## Slide 67: History of neural network
first introduced in 1943 by Warren McCulloch, a neurophysiologist, and a mathematician Walter Pitts
In 1949, Donald Hebb published a book, “The Organization of Behavior,” where he formulated the classical Hebbian rule, which is proved to be the basis of almost all neural learning procedures
John Hopfield invented associative neural network in 1982, which is now more commonly known as Hopfield Network
backpropagation algorithm, a generalization of Widrow-Hoff learning algorithm, was invented by Rumelhart, Hinton and Williams  renaissance of research in neural network

## Slide 68: Types of NN
Feedforward NN (Svozil et al. 1997): conveys the information in one direction
Radial basis function network (Orr 1996): uses the Gaussian radial basis function
Recurrent NN (Bodén 2001): local feedback connections between the input and outputs, and so forth
Fuzzy-neural (Liu and Li 2004), wavelet (He et al. 2004), associative-memory (Bicciato et al. 2001), modular (Happel and Murre 1994) and hybrid (Zhang and Yuen 2013, Rovithakis et al. 2004) neural networks

## Slide 69: Feedforward NN model
Neurons or nodes: basic processing units in NN
  they can be grouped into different layers such as input layer, output layer and hidden layer
Input layer: receiving input data from outside
Output layer: send processed data out of the NN (prediction)
Hidden layer: between input and output layers, no interaction with outside (not shown to users)
Feedforward NN
  information only moves in forward direction from input layer, through hidden layer and to output layer
  no feedback or flow within layers

## Slide 70: Illustration of feedforward NN model

## Slide 71: Illustration of feedforward NN model
Feedforward: information flows from input layer to hidden layer to output layer
Parameters
  Weight: interconnection parameter between different nodes,
  Bias: threshold value added after weighted sum of inputs from previous layer,
Transfer (activation) function
  Integrate the linear combination of information from the previous layers using weights and bias

## Slide 72: Training process
finding the optimal parameters, weights and biases, such that the network model accurately represents the relationship between inputs and outputs
backpropagation: propagates the error between training data and the network outputs backward
  optimization process to find the best weights and biases to minimize the mean square error between network predictions and training data
  parameters (gradient or Jacobian) for hidden weights and output bias (output layer) are updated first
  then, parameters for input weights and hidden biases (hidden layer) are updated next based on the updated parameters in the output layer

## Slide 73: Feedforward mechanism
Relationship between input nodes and hidden nodes :
  input weight matrix
  hidden bias vector
  transfer function in the hidden layer
Relationship between hidden nodes and output nodes :
  hidden weight matrix
  output bias vector
  transfer function in the output layer
We will consider case only

## Slide 74: Training process
First, the network structure must be decided
  The number of input nodes, hidden nodes, and output nodes
Training process determines all weights, and , and all biases, and
Training data:
Minimize the error between and
  This is similar to regression
  In general, need to solve optimization problem for nonlinear transfer functions

## Slide 75: Training process cont.
Apply training data to ,
  matrix of training input data
  : hidden bias matrix
  : matrix of hidden layer outputs
  : vector of network simulation outputs
  : hidden weight row vector
  : output bias vector

## Slide 76: Ex) FFNN with linear transfer function
Two input nodes, one hidden node, linear transfer function and ()
  Hidden layer:
  Output layer:
  Equivalent one-layer network model

## Slide 77: Training process with pure linear transfer function
When and
  One-layer NN model with being input weights and being the output bias
  Multi-layer NN model with pure linear transfer function can be converted into a single-layer NN model

## Slide 78: Input data in time-domain NN
We consider a dynamic response of a system. Input = time, output = QoI
Data
Use 3 previous data as input for predicting
Input matrix Output vector

## Slide 79: Transfer functions
  characterize the relationship between two adjacent layers
  should be differentiable: need for backpropagation training process
  Pure linear function:
  Sigmoid function:

## Slide 80: Ex) Complexity of NN model
2-layer NN model: 1 input node, 1 (or 5) hidden node, and 1 output node
  Generate random weights and biases from
  Repeat 5 times:
1-hidden node
5-hidden nodes

## Slide 81: Backpropagation process
  a training method to determine weights and biases through a learning/optimization algorithm by backward propagation of the errors between the training data and the network outputs
  layer-by-layer updating
  Data:
Setting initial values of parameters (weights & biases)
  Too large initial weights  fall in the saturation region
  Too small initial weights  low learning rate
  Usually random number in , or fixed value of 1
  For prognostics, degradation is monotonic and stay in positive value
  Increasing degradation , decreasing

## Slide 82: Backpropagation process cont.
Feedforward to simulation outputs using inputs
Mean-squared-error (MSE) between training output and simulation output
Using optimization algorithm and gradients of MSE, calculate and of the output layer
  Gradient descent or Levenberg-Marquardt (LM) algorithm
Calculate and of the hidden layer
  and depend on and

## Slide 83: Backpropagation process cont.
Update the weights and biases of NN model
Repeat Steps 1 ~ 6 until satisfying a stopping criterion

## Slide 84: Matlab functions for feedforward NN
define a network model  set up configurations  train the network model  prediction with different inputs
feedforwardnet: creates a two-layer network model with user-defined number of hidden nodes
  Tangent sigmoid function: default activation function for hidden layers
  Pure linear function: default activation function of output layers
configure: Optional step to normalize input and output data and assigns them to each node
  Normalization between -1 and 1
  Randomly select initial values of weights and biases
  Use configuration to assign user-defined initial values

## Slide 85: Matlab functions for feedforward NN
train: trains the network model with the LM backpropagation for training method and the MSE for the error function
  train uses all data at once
  adapt uses data one-by-one, good for online learning
sim: simulates/predicts the network outputs at new inputs based on the identified weights and biases during the training process

## Slide 86: Stopping criterion based on validation error
  Randomly divide data: training (70%), validation (15%), test (15%)
  use training set to update the weights and biases based on their error
  The error of the training set keeps decreasing, and the error in the validation set also decreases: the training process goes well
  The error in the validation set starts increasing after some phase of training process, i.e., good performance at the training set but bad performance at the validation set (new points, prediction points): the network model overfits the training data
  Therefore, the training process stops when the validation error starts increasing
  The test data sets are not used during the training process but used for testing the prediction accuracy with trained parameters

## Slide 87: Ex) Feedforward NN model
Predict y at using one hidden-node NN
Matlab code
  x=[0 5 10 15 20]; %[1 x 5] training input data
  y=[1 0.99 0.99 0.94 0.95]; %[1 x 5] training output data
  nh=1; % num. of hidden node
  net=feedforwardnet(nh); % create two-layer network model
  net=configure(net,x,y); % this is optional
  [netModel,trainRecor]=train(net,x,y); % train the model ‘net’
  xNew=-5:0.1:25; % new input points
  z=sim(netModel,xNew); % simulation results

## Slide 88: Ex) Feedforward NN model cont.
Initial values are randomly generated and stored in net
  net.iw (input weights), net.lw (hidden weights), net.b (biases)
netModel is the trained network model
Available data is too small for training
  # of training data (5) # of parameters (4): not accurate
  70% of training data > 2* # of parameters
epoch: one complete presentation of the data set to be learned to a learning machine
  Iteration: the number of batches or steps through partitioned packets of the training data, needed to complete one epoch

## Slide 89: Ex) Feedforward NN model cont.
Training records
  trainRecor.trainInd (training set), trainRecor.valInd (validation set), and trainRecor.testInd (test set)
  plotperf(trainRecor); performance (MSE) plot for 3 sets
  trainRecor.num_epochs = 8 (total available epochs)
  trainRecor.best_epoch = 2 (best epochs)
  trainRecor.best_vperf: best performance
  bestE=trainRecor.best_epoch;
  bestP=trainRecor.best_vperf;
  hold on; plot(bestE,bestP,'o');

## Slide 90: Ex) Feedforward NN model cont.
Prediction (simulation)
  Using the trained network model, predict the degradation at various times
  xNew=-5:0.1:25; % new input points
  z=sim(netModel,xNew); % simulation results

## Slide 91: Ex) Feedforward NN model cont.
Uncertainty
  the initial values of parameters are assigned differently. Also, the train, validation, and test sets change when the training is restarted. These two are the sources of uncertainty in the neural network process and make different results
Simulation #5

## Slide 92: NN: Matlab Code for Neural Network
Problem definition (similar to GP)
function rul=NN(TransFunc,nh,outliCrite)
clear global;
global DegraUnit TimeUnit time y thres signiLevel ns ny nt
%=== PROBLEM DEFINITION 1 (Required Variables) ==============
WorkName=' '; % work results are saved by WorkName
DegraUnit=' '; % degradation unit
TimeUnit=' '; % time unit (Cycles, Weeks, etc.)
time=[ ]'; %[cv]: time at both measurement and prediction
y=[ ]'; %[ny x 1]: measured data
nT= ; % num. of training set including the current one
nt=[ ]';%[nT x 1]: num. of training data in each training set
thres= ; % threshold (critical value)
degraTrue=[ ]'; %[cv]: true values of degradation
signiLevel= ; % significance level for C.I. and P.I.
ns= ; % number of repetition for NN process
%=== PROBLEM DEFINITION 2 (Training Matrix) =================
xTrain=[ ]; yTrain=[ ];
%============================================================

## Slide 93: NN Matlab Code cont.
Training network model
% % % PROGNOSIS using NN
ny=length(y);
for i=1:ns; %% NN Process
disp(['repetition: ' num2str(i) '/' num2str(ns)]);
% create FFNN
net=feedforwardnet(nh);
net.layers.transferfcn=TransFunc;
net.divideParam.valRatio=0.3; net.divideParam.testRatio=0;
% train FFNN
[netModel,trainRecod]=train(net,xTrain',yTrain');
%=== PROBLEM DEFINITION 2 (Input Matrix for Prediction) =====
for k=1:length(time(ny:end)); %% Degradation Prediction
xNew=[ ];
zHat(k,i)=sim(netModel,xNew');
end;
%============================================================
end

## Slide 94: NN Matlab Code cont.
Prediction
z1=zHat(end,:); %% Prediction Results Regulation
loca1=find(abs(z1-mean(z1)) < outliCrite*std(z1));
i0=1;
for i=1:ns;
if y(1)-y(nt(1))>0; z2=wrev(zHat(:,i));
else z2=zHat(:,i);
end;
if issorted(z2)==1; loca2(i0)=i; i0=i0+1; end
end
loca=intersect(loca1,loca2); %% Final Results
degraPredi=zHat(:,loca);
ns=size(degraPredi,2);
disp(['Final num. of samples: ' num2str(ns)])
% % % POST-PROCESSING
rul=POST([],degraPredi,degraTrue); %% RUL & Result Disp
Name=[WorkName ' at ' num2str(time(ny)) '.mat']; save(Name);
end

## Slide 95: NN Implementation of Battery Prognostics
Problem definition
  ns: number of NN repetitions (~ 30)
  Matlab NN automatically normalize inputs and outputs
  Train data
  Prediction time
Calling convention
  purelin is used for activation function for both hidden and output
  outliCrite = 2: results beyond will be eliminated (outlier)
xTrain=time(1:length(y)); yTrain=y;
xNew=time(ny-1+k);
rul=NN({'purelin'; 'purelin'},1,2);

## Slide 96: NN Implementation of Battery Prognostics cont.
Prognostics using NN
  Create the network model net and assign activation functions
  Use 70% training, 30% validation, no test data
Training parameters
  Early stopping criteria to prevent overfitting
  cannot control the underfitting
% create FFNN
net=feedforwardnet(nh);
net.layers.transferfcn=TransFunc;
net.divideParam.valRatio=0.3; net.divideParam.testRatio=0;
% train FFNN
[netModel,trainRecod]=train(net,xTrain',yTrain');

## Slide 97: NN Implementation of Battery Prognostics cont.
Regulations
  the outliers deviated from the majority of prediction results are determined based on the results at the last prediction step
  Sample out of are removed
  predictions do not monotonically increase/decrease are removed
z1=zHat(end,:); %% Prediction Results Regulation
loca1=find(abs(z1-mean(z1)) < outliCrite*std(z1));
i0=1;
for i=1:ns;
if y(1)-y(nt(1))>0; z2=wrev(zHat(:,i));
else z2=zHat(:,i);
end;
if issorted(z2)==1; loca2(i0)=i; i0=i0+1; end
end
loca=intersect(loca1,loca2); %% Final Results

## Slide 98: NN Implementation of Battery Prognostics cont.
under-fitting
Battery degradation (NN)
Crack growth (NN)

## Slide 99: NN Implementation of Battery Prognostics cont.
Postprocessing
  Larger uncertainty in RUL because NN has more parameters than GP
plot(time(ny:end),zHat,'m'); plot(time(ny:end),degraPredi,'color',[.5 .5 .5]);

## Slide 100: Practical Use of Data-Driven Approaches

## Slide 101: Inputs
Time is input, but
  work well for a simple problem with one data set
  Not useful when training data sets obtained under different usage conditions
In order to be practical …
  degradation levels are used as both input and output
  The current degradation state as an output can be expressed with several previous degradation states as the inputs
  utilize the information included in different degradation rates from the different data sets
  having previous degradation states as inputs can allow to use a simpler functional form
We will use crack growth problem for demonstration

## Slide 102: Crack Growth Prognostics
26 training data are generated from true model parameters
  Run-to-fail set:
16 prediction data: same parameters and loading
Inputs
  3 previous crack sizes as inputs to predict

## Slide 103: Short- versus Long-term Prediction
Short-term prediction
  One-step ahead prediction (prediction using real data)
  Use to predict
  Not able to predict degradation at future time
Long-term prediction
  Use predictions at previous times to predict future
  Use to predict
  since predictions are used for inputs, the accuracy will be worse than short-term prediction
  but it allows to predict the degradation in long future time

## Slide 104: Matlab Codes for Crack Growth
Problem definition
WorkName='Crack_GP'; % or 'Crack_NN'
DegraUnit='Crack size (m)';
TimeUnit='Cycles';
time=[0:100:2500, 0:100:1600, 1700:100:4000]';
y=[0.01 0.0104 0.0107 0.0111 0.0116 0.0120 0.0125 ...
0.0131 0.0137 0.0143 0.0150 0.0158 0.0166 0.0176 ...
0.0186 0.0198 0.0211 0.0226 0.0243 0.0263 0.0287 ...
0.0314 0.0347 0.0387 0.0437 0.0501 ...
0.0100 0.0103 0.0106 0.0109 0.0112 0.0116 0.012 0.0124 ...
0.0128 0.0133 0.0138 0.0143 0.0149 0.0155 0.0162 0.0169]';
nT=2;
nt=[26 16]';
thres=0.05;
mTrue=3.8; cTrue=1.5e-10; aTrue=0.01; dsig=75; t=0:100:3500;
degraTrue=(t'.*cTrue.*(1-mTrue./2).*(dsig*sqrt(pi)).^mTrue...
+aTrue.^(1-mTrue./2)).^(2./(2-mTrue));
signiLevel=5;
ns=5e3; % or 30 for NN

## Slide 105: Matlab Codes for Crack Growth cont.
Training degradation data
  26 run-to-fail data at 79 MPa + 16 data at 75 MPa from current system
  Prediction future time (1700:100:4000)
Inputs: 3 previous degradation data
GP problem definition (training)
nx=3; % num. of previous data as the input
y0=(y-min(y))/(max(y)-min(y)); % normalization of data
nm=size(y,2); a=0; b=0;
for l=1:nT;
for k=1:nt(l)-nx;
xTrain(k+a,1:nx*nm)=reshape(y0(k+b:(k-1)+nx+b,:),1,nx*nm);
yTrain(k+a,:)=y0(k+nx+b,:);
end; a=size(xTrain,1); b=sum(nt(1:l));
end

## Slide 106: Matlab Codes for Crack Growth cont.
NN problem definition (training, no normalization)
Additional modification for GP
  Change exponent 2 to 1.9 (to prevent singularity in the correlation matrix)
nx=3; % num. of previous data as the input
nm=size(y,2); a=0; b=0;
for l=1:nT;
for k=1:nt(l)-nx;
xTrain(k+a,1:nx*nm)=reshape(y(k+b:(k-1)+nx+b,:),1,nx*nm);
yTrain(k+a,:)=y(k+nx+b,:);
end; a=size(xTrain,1); b=sum(nt(1:l));
end
R(k,l)=exp(-(norm(xTrain(k,:)-x0(l,:))/h)^1.9);

## Slide 107: Matlab Codes for Crack Growth cont.
GP Problem definition 2 (Prediction Stage)
NN Problem definition 2 (Prediction Stage, no-normalization)
input=y0(end-nx:end,:);
for k=1:length(time(ny:end));
xNew=reshape(input(k:(k-1)+nx,:),1,nx*nm);
[zMean(k,:),zSig(k,:)]= ...
GPSIM(xNew,funcOrd,hH,R,thetaH,sigmaH);
if k>1 input(k+nx,:)=zMean(k,:); end
end;
input=y(end-nx:end,:);
for k=1:length(time(ny:end));
xNew=reshape(input(k:(k-1)+nx,:),1,nx*nm);
zHat(k,i)=sim(netModel,xNew');
if k>1, input(k+nx,:)=zHat(k,i); end
end;

## Slide 108: Matlab Codes for Crack Growth cont.
Calling convention
  GP
  NN
rul=GP(1,0.1);
rul=NN({'purelin'; 'purelin'},1,2);

## Slide 109: Results
Linear global function (GP) and activation function (NN)  still can predict nonlinear degradation
  because the relation between previous three degradation data and the current degradation data can be captured by a linear function
GP is accurate with small prediction uncertainty
  Reversed trend after 3000 cycles because of extrapolation
GP
NN

## Slide 110: Results cont.
NN: out of 30 repetitions
  19 failed to satisfy 2 regulations: outliers and monotonicity
  Larger prediction uncertainty than GP
RUL prediction

## Slide 111: Issues in Data-Driven Prognostics

## Slide 112: Model-Form Adequacy for GP
Global function
  performance largely depends on global and covariance functions
  Conventional interpolation: global function is not important (ordinary Kriging)
  Prognostics: extrapolation, global function is as important as covariance fn
  not much literature on selecting or updating the global function to improve the prediction capability in the extrapolation region
Covariance function
  determine GP simulation quality for entire regions
  non-stationary covariance function: adapts to variable smoothness by adding or multiplying simple covariance functions
  Non-stationary covariance function requires more parameters

## Slide 113: Model-Form Adequacy for NN
Network model = selecting the number of hidden nodes, hidden layers and input nodes
Determining hidden layers/nodes
  one or two hidden layers are commonly used
  It is possible to determine the optimal number of hidden nodes using MSE
  Or, measuring complexity of function to determine the number of nodes
Determining input nodes
  Input nodes = available information, time, loading conditions, and degradation data
  Several past degradation data can be used as inputs
there is no universal procedure to establish a proper NN model

## Slide 114: Optimal Parameter Estimation for GP
Scale parameters (hyper-parameters)
  determine the smoothness of the GP function
  Large makes the prediction smooth; becomes singular with too large
  Generally, is determined by maximizing likelihood function
  Optimal is difficult to find, and optimum is not always the best selection
  can be considered as a distribution (work better than deterministic )
No strategy to find best for prognostics (extrapolation)
  Many SHM data with small intervals  small  extrapolation quickly converge to the global function

## Slide 115: Optimal Parameter Estimation for NN
Determining weights and biases
  Complex behavior requires a greater number of nodes  a greater number of weights and biases  require mode training data
Difficulty using backpropagation algorithm
  the global optimum is extremely difficult to find in the case of many parameters
  the convergence rate is very low and depends on the initial estimates
Algorithmic improvement
  dynamic self-adaptation algorithm, simulated annealing algorithm, combined genetic and differential evolution algorithm
probabilistic approaches (Bayesian learning technique)
  Represent uncertainty in the parameters
  finding optimal weights and biases is still challenging

## Slide 116: Quality of Degradation Data
uncertainty caused by bias and noise in data is an important issue regardless of prognostics approaches
the bias cannot be handled with data-driven approaches because there are no parameters related to it
data quality issues for noise will be discussed in Chapter 6

## Slide 117: Quality of Degradation Data in GP
Large # of training data are not always good for GP
  Difficult to calculate the inverse of covariance matrix (may cause singularity)
  Only a portion of whole data can be used
  Or approximation of the inverse of covariance matrix
When data include noise
  GP generally assumes that data are accurate
  Nugget effect represents noise in data by adding diagonal terms of the covariance matrix
  Nugget STD is coupled with h  difficult to uniquely identify it

## Slide 118: Quality of Degradation Data in NN
Uncertainty in prediction results
Difficult to find global optimum of parameters
  measurement noise, a small number of data compared to the number of parameters, and the complexity of damage growth, which can yield a significant error in prediction results
Bootstrapping
  running Matlab NN toolbox several times because Matlab uses different subsets of the training data to obtain weights and biases
  Also, use different (randomly generated) initial parameters
Systematically handling uncertainty
  probabilistic neural network (PNN)
  Bayesian NN