## Slide 1: CHAP 2 Nonlinear Finite Element Analysis Procedures
Nam-Ho Kim

## Slide 2: Goals
What is a nonlinear problem?
How is a nonlinear problem different from a linear one?
What types of nonlinearity exist?
How to understand stresses and strains
How to formulate nonlinear problems
How to solve nonlinear problems
When does nonlinear analysis experience difficulty?

## Slide 3: Nonlinear Structural Problems
What is a nonlinear structural problem?
  Everything except for linear structural problems
  Need to understand linear problems first
What is linearity?
Example: fatigue analysis
Input x
(load, heat)
Output y
(displ, temp)
x1
y1
x2
y2
2x1
2y1
2x1 +3x2
2y1+3y2
x1
x2
Y

## Slide 4: What is a linear structural problem?
Linearity is an approximation
Assumptions:
  Infinitesimal strain (<0.2%)
  Infinitesimal displacement
  Small rotation
  Linear stress-strain relation
F/2
F/2
A0
A
L0
dL
L
E
s
e
s = Ee
Force
Stress
Strain
Displacement
Linear
Linear
Linear
Global
Global
Local
Local

## Slide 5: Observations in linear problems
Which one will happen?
Will this happen?
M
M
F
Truss
Truss

## Slide 6: What types of nonlinearity exist?
It is at every stage of analysis

## Slide 7: Linear vs. Nonlinear Problems
Linear Problem:
  Infinitesimal deformation:
  Linear stress-strain relation:
  Constant displacement BCs
  Constant applied forces
Nonlinear Problem:
  Everything except for linear problems!
  Geometric nonlinearity: nonlinear strain-displacement relation
  Material nonlinearity: nonlinear constitutive relation
  Kinematic nonlinearity: Non-constant displacement BCs, contact
  Force nonlinearity: follow-up loads
Undeformed coord.
Constant

## Slide 8: Nonlinearities in Structural Problems
More than one nonlinearity can exist at the same time
Displacement
Strain
Stress
Prescribed displacement
Applied force
Nonlinear displacement-strain
Nonlinear stress-strain
Nonlinear displ. BC
Nonlinear force BC

## Slide 9: Geometric Nonlinearity
Relations among kinematic quantities (i.e., displacement, rotation and strains) are nonlinear
Displacement-strain relation
  Linear:
  Nonlinear:
0.0 0.2 0.4 0.6 0.8 1.0
Normalized couple
8.
6.
4.
2.
0.
Tip displacement
C0
C1
C2
C3
When du/dx is small
H.O.T. can be ignored

## Slide 10: Geometric Nonlinearity cont.
Displacement-strain relation
  E has a higher-order term
  (du/dx) << 1  e(x) ~ E(x).
Domain of integration
  Undeformed domain W0
  Deformed domain Wx
0 0.05 0.10 0.15 0.20 0.25 0.30
du/dx
0.35
0.30
0.25
0.20
0.15
0.10
0.05
0
Strain
e
E
Deformed domain is unknown

## Slide 11: Material Nonlinearity
Linear (elastic) material
  Only for infinitesimal deformation
Nonlinear (elastic) material
  [D] is not a constant but depends on deformation
  Stress by differentiating strain energy density U
  Linear material:
  Stress is a function of strain (deformation): potential, path independent
1
e
s
E
e
s
E
Linear spring
Nonlinear spring
Linear and nonlinear elastic spring models
More generally, {s} = {f(e)}

## Slide 12: Material Nonlinearity cont.
Elasto-plastic material (energy dissipation occurs)
  Friction plate only support stress up to sy
  Stress cannot be determined from stress alone
  History of loading path is required: path-dependent
Visco-elastic material
  Time-dependent behavior
  Creep, relaxation
Visco-elastic spring model
s
E
h
time
s
Ee
Elasto-plastic spring model
s
E
sY
e
s
E
sY

## Slide 13: Boundary and Force Nonlinearities
Nonlinear displacement BC (kinematic nonlinearity)
  Contact problems, displacement dependent conditions
Nonlinear force BC (Kinetic nonlinearity)
Contact boundary
dmax
Displacement
Force

## Slide 14: Mild vs. Rough Nonlinearity
Mild Nonlinear Problems
  Continuous, history-independent nonlinear relations between stress and strain
  Nonlinear elasticity, Geometric nonlinearity, and deformation-dependent loads
Rough Nonlinear Problems
  Equality and/or inequality constraints in constitutive relations
  History-dependent nonlinear relations between stress and strain
  Elastoplasticity and contact problems

## Slide 15: Nonlinear Finite Element Equations
Equilibrium between internal and external forces
Kinetic and kinematic nonlinearities
  Appears on the boundary
  Handled by displacements and forces (global, explicit)
  Relatively easy to understand (Not easy to implement though)
Material & geometric nonlinearities
  Appears in the domain
  Depends on stresses and strains (local, implicit)
Linear problems
Stress Strain
Loads

## Slide 16: Solution Procedure
We can only solve for linear problems …

## Slide 17: Example – Nonlinear Springs
Spring constants
  k1 = 50 + 500u k2 = 100 + 200u
Governing equation
  Solution is in the intersection between two zero contours
  Multiple solutions may exist
  No solution exists in a certain situation
k1
k2
u1
u2
F
P1
P2

## Slide 18: Solution Procedure
Linear Problems
  Stiffness matrix K is constant
  If the load is doubled, displacement is doubled, too
  Superposition is possible
Nonlinear Problems
  How to find d for a given F?
F
d
di
KT
2F
2d
d
K
F
Incremental Solution Procedure

## Slide 19: Newton-Raphson Method
Most popular method
Assume di at i-th iteration is known
Looking for di+1 from first-order Taylor series expansion
  : Jacobian matrix or Tangent stiffness matrix
Solve for incremental solution
Update solution
di
di+1
d
Ddi+1
F
P(d)
di+2
dn
Solution
P(di)
P(di+1)

## Slide 20: N-R Method cont.
Observations:
  Second-order convergence near the solution (Fastest method!)
  Tangent stiffness is not constant
  The matrix equation solves for incremental displacement
  RHS is not a force but a residual force
  Iteration stops when conv < tolerance
Or,

## Slide 21: N-R Algorithm
Set tolerance = 0.001, k = 0, max_iter = 20, and initial estimate u = u0
Calculate residual R = f – P(u)
Calculate conv. If conv < tolerance, stop
If k > max_iter, stop with error message
Calculate Jacobian matrix KT
If the determinant of KT is zero, stop with error message
Calculate solution increment u
Update solution by u = u + u
Set k = k + 1
Go to Step 2

## Slide 22: Example – N-R Method
Iteration 1

## Slide 23: Example – N-R Method cont.
Iteration 2
Iteration 3

## Slide 24: Example – N-R Method cont.
Iteration 4
Iteration
Residual
Quadratic convergence
Iter | ¦¦R¦¦
0 | 17.263
1 | 4.531
2 | 0.016
3 | 0.0

## Slide 25: When N-R Method Does Not Converge
Difficulties
  Convergence is not always guaranteed
  Automatic load step control and/or line search techniques are often used
  Difficult/expensive to calculate
di
di+1
d
F
P(d)
di+2
dn
Solution

## Slide 26: When N-R Method Does Not Converge cont.
Convergence difficulty occurs when
  Jacobian matrix is not positive-definite
  Bifurcation & snap-through require a special algorithm
A
B
C
D
E
A
B
C
D
E
Displacement
Force
F
FB
FC
P.D. Jacobian: in order to increase displ., force must be increased

## Slide 27: Modified N-R Method
Constructing and solving is expensive
Computational Costs (Let the matrix size be N x N)
  L-U factorization ~ N3
  Forward/backward substitution ~ N
Use L-U factorized repeatedly
More iteration is required, but each iteration is fast
More stable than N-R method
Hybrid N-R method
di
di+1
d
F
P(d)
dn
Solution

## Slide 28: Example – Modified N-R Method
Solve the same problem using modified N-R method
Iteration 1

## Slide 29: Example – Modified N-R Method cont.
Iteration 2
Iteration
Residual
Iter | ¦¦R¦¦
0 | 17.263
1 | 4.5310
2 | 0.3584
3 | 0.0831
4 | 0.0204
5 | 0.0051
6 | 0.0013
7 | 0.0003

## Slide 30: Incremental Secant Method
Secant matrix
  Instead of using tangent stiffness, approximate it using the solution from the previous iteration
  At i-th iteration
  The secant matrix satisfies
  Not a unique process in high dimension
Start from initial KT matrix, iteratively update it
  Rank-1 or rank-2 update
  The textbook has Broyden’s algorithm (Rank-1 update)
  Here we will discuss BFGS method (Rank-2 update)
F
d0
d1
d
P(d)
dn
Solution
d2
d3
Secant stiffness

## Slide 31: Incremental Secant Method cont.
BFGS (Broyden, Fletcher, Goldfarb and Shanno) method
  Stiffness matrix must be symmetric and positive-definite
  Instead of updating K, update H (saving computational time)
Become unstable when the No. of iterations is increased

## Slide 32: Incremental Force Method
N-R method converges fast if the initial estimate is close to the solution
Solid mechanics: initial estimate = undeformed shape
Convergence difficulty occurs when the applied load is large (deformation is large)
IFM: apply loads in increments. Use the solution from the previous increment as an initial estimate
  Commercial programs call it “Load Increment” or “Time Increment”

## Slide 33: Incremental Force Method cont.
Load increment does not have to be uniform
  Critical part has smaller increment size
Solutions in the intermediate load increments
  History of the response can provide insight into the problem
  Estimating the bifurcation point or the critical load
  Load increments greatly affect the accuracy in path-dependent problems

## Slide 34: Load Increment in Commercial Software
Use “Time” to represent load level
  In a static problem, “Time” means a pseudo-time
  Required Starting time, (Tstart), Ending time (Tend) and increment
  Load is gradually increased from zero at Tstart and full load at Tend
  Load magnitude at load increment Tn:
Automatic time stepping
  Increase/decrease next load increment based on the number of convergence iteration at the current load
  User provide initial load increment, minimum increment, and maximum increment
  Bisection of load increment when not converged

## Slide 35: Force Control vs. Displacement Control
Force control: gradually increase applied forces and find equilibrium configuration
Displ. control: gradually increase prescribed displacements
  Applied load can be calculated as a reaction
  More stable than force control.
  Useful for softening, contact, snap-through, etc.
u1
u2
u
F
P(u)
un
F2
F3
Fn
u3
F1
uA
uB
u
F
P(u)
uD
FB
FC
uC
FA

## Slide 36: Nonlinear Solution Steps
Initialization:
Residual Calculation
Convergence Check (If converged, stop)
Linearization
  Calculate tangent stiffness
Incremental Solution:
  Solve
State Determination
  Update displacement and stress
Go To Step 2

## Slide 37: Nonlinear Solution Steps cont.
State determination
  For a given displ dk, determine current state (strain, stress, etc)
  Sometimes, stress cannot be determined using strain alone
Residual calculation
  Applied nodal force − Nodal forces due to internal stresses
Weak form:
Discretization:
Residual:

## Slide 38: Example – Linear Elastic Material
Governing equation (Scalar equation)
Collect
Residual
Linear elastic material
d
F
KT

## Slide 39: Example – Nonlinear Bar
Rubber bar
Discrete weak form
Scalar equation
0 0.01 0.02 0.03 0.04 0.05
Strain
120
100
80
60
40
20
0
Stress
F = 10kN
L = 1m
1
2
x

## Slide 40: Example – Nonlinear Bar cont.
Jacobian
N-R equation
Iteration 1
Iteration 2

## Slide 41: N-R or Modified N-R?
It is always recommended to use the Incremental Force Method
  Mild nonlinear: ~10 increments
  Rough nonlinear: 20 ~ 100 increments
  For rough nonlinear problems, analysis results depends on increment size
Within an increment, N-R or modified N-R can be used
  N-R method calculates KT at every iteration
  Modified N-R method calculates KT once at every increment
  N-R is better when: mild nonlinear problem, tight convergence criterion
  Modified N-R is better when: computation is expensive, small increment size, and when N-R does not converge well
Many FE programs provide automatic stiffness update option
  Depending on convergence criteria used, material status change, etc

## Slide 42: Accuracy vs. Convergence
Nonlinear solution procedure requires
  Internal force P(d)
  Tangent stiffness
  They are often implemented in the same routine
Internal force P(d) needs to be accurate
  We solve equilibrium of P(d) = F
Tangent stiffness KT(d) contributes to convergence
  Accurate KT(d) provides quadratic convergence near the solution
  Approximate KT(d) requires more iteration to converge
  Wrong KT(d) causes lack of convergence

## Slide 43: Convergence Criteria
Most analysis programs provide three convergence criteria
  Work, displacement, load (residual)
  Work = displacement * load
  At least two criteria needs to be converged
Traditional convergence criterion is load (residual)
  Equilibrium between internal and external forces
Use displacement criterion for load insensitive system
Force
Displacement
Use load criterion
Use displacement criterion

## Slide 44: Solution Strategies
Load Step (subcase or step)
  Load step is a set of loading and boundary conditions to define an analysis problem
  Multiple load steps can be used to define a sequence of loading conditions
LS1
LS2
Load
Time
NASTRAN
SPC = 1
SUBCASE 1
LOAD = 1
SUBCASE 2
LOAD = 2

## Slide 45: Solution Strategies
Load Increment (substeps)
  Linear analysis concerns max load
  Nonlinear analysis depends on load path (history)
  Applied load is gradually increased within a load step
  Follow load path, improve accuracy, and easy to converge
Convergence Iteration
  Within a load increment, an iterative method (e.g., NR method) is used to find nonlinear solution
  Bisection, linear search, stabilization, etc
Fa
F
u
1
2
3
4
5
0
0.2
0.4
0.6
0.8
1
-100
-50
0
50
100
150
200
250
300
Displacement
Force
Loading
Unloading

## Slide 46: Solution Strategies cont.
Automatic (Variable) Load Increment
  Also called Automatic Time Stepping
  Load increment may not be uniform
  When convergence iteration diverges, the load increment is halved
  If a solution converges in less than 4 iterations, increase time increment by 25%
  If a solution converges in more than 8 iterations, decrease time increment by 25%
Subincrement (or bisection)
  When iterations do not converge at a given increment, analysis goes back to previously converged increment and the load increment is reduced by half
  This process is repeated until max number of subincrements

## Slide 47: When nonlinear analysis does not converge
NR method assumes a constant curvature locally
When a sign of curvature changes around the solution, NR method oscillates or diverges
Often the residual changes sign between iterations
Line search can help to converge

## Slide 48: When nonlinear analysis does not converge
Displacement-controlled vs. force-controlled procedure
  Almost all linear problems are force-controlled
  Displacement-controlled procedure is more stable for nonlinear analysis
  Use reaction forces to calculate applied forces
A
B
C
D
E
F
A
B
C
D
E
Displacement
Force
FB
FC

## Slide 49: When nonlinear analysis does not converge
Mesh distortion
  Most FE programs stop analysis when mesh is distorted too much
  Initial good mesh may be distorted during a large deformation
  Many FE programs provide remeshing capability, but it is still inaccurate or inconvenient
  It is best to make mesh in such a way that the mesh quality can be maintained after deformation (need experience)
Initial mesh

## Slide 50: MATLAB Code for Nonlinear FEA

## Slide 51: NLFEA.m
Nonlinear finite element analysis program
  Incremental force method with N-R method
  Bisection method when N-R is failed to converge
  Can solve for linear elastic, hyperelastic and elasto-plastic material nonlinearities with large deformation
Global arrays
Name | Dimension | Contents
GKF | NEQ x NEQ | Tangent matrix
FORCE | NEQ x 1 | Residual vector
DISPTD | NEQ x 1 | Displacement vector
DISPDD | NEQ x 1 | Displacement increment
SIGMA | 6 x 8 x NE | Stress at each integration point
XQ | 7 x 8 x NE | History variable at each integration point

## Slide 52
Stop
Update history variables
Print stress & displacement
T = T + DT
Bisection control
Final time?
Input data
Increase load & BC
ITER = 0
Calculate R & K
Displacement BC
Converged?
Max ITER?
Solve DU = K\R
U = U + DU
ITER=ITER + 1
T = T – DT
DT = DT/2
Yes
No
Yes
No
Yes
No

## Slide 53: NLFEA.m cont.
Nodal coordinates and element connectivity
  the node numbers are in sequence
  nodal coordinates in XYZ(NNODE , 3)
  eight-node hexahedral elements LE(NELEN, 8)
Applied forces and prescribed displacements
  EXTFORCE(NFORCE, 3): [node, DOF, value] format
  SDISPT(NDISPT, 3)
Load steps and increments
  TIMS(NTIME,5): [Tstart, Tend, Tinc, LOADinit, LOADfinal] format
Material properties
  Mooney-Rivlin hyperelasticity (MID = -1), PROP = [A10, A01, K]
  infinitesimal elastoplasticity (MID = 1), PROP = [LAMBDA, MU, BETA, H, Y0]

## Slide 54: NLFEA.m cont.
Control parameters
  ITRA: maximum number of convergence iterations
  if residual > ATOL, then solution diverges, bisection starts
  The total number of bisections is limited by NTOL
  The convergence iteration converges when residual < TOL
  Program prints out results to NOUT after convergence
function NLFEA(ITRA,TOL,ATOL,NTOL,TIMS,NOUT,MID,PROP,EXTFORCE,SDISPT,XYZ,LE)
%***********************************************************************
% MAIN PROGRAM FOR HYPERELASTIC/ELASTOPLASTIC ANALYSIS
%***********************************************************************

## Slide 55: Extension of a Single Element Example
%
% Nodal coordinates
XYZ=[0 0 0;1 0 0;1 1 0;0 1 0;0 0 1;1 0 1;1 1 1;0 1 1];
%
% Element connectivity
LE=[1 2 3 4 5 6 7 8];
%
% External forces [Node, DOF, Value]
EXTFORCE=[5 3 10.0; 6 3 10.0; 7 3 10.0; 8 3 10.0];
%
% Prescribed displacements [Node, DOF, Value]
SDISPT=[1 1 0;1 2 0;1 3 0;2 2 0;2 3 0;3 3 0;4 1 0;4 3 0];
%
% Load increments [Start End Increment InitialLoad FinalLoad]
TIMS=[0.0 0.5 0.1 0.0 0.5; 0.5 1.0 0.1 0.5 1.0]';
%
% Material properties
%PROP=[LAMBDA MU BETA H Y0]
MID=1;
PROP=[110.747, 80.1938, 0.0, 5., 35.0];
%
% Set program parameters
ITRA=20; ATOL=1.0E5; NTOL=5; TOL=1E-6;
%
% Calling main function
NOUT = fopen('output.txt','w');
NLFEA(ITRA, TOL, ATOL, NTOL, TIMS, NOUT, MID, PROP, EXTFORCE, SDISPT, XYZ, LE);
fclose(NOUT);

## Slide 56: Tension of Elastoplastic Bar Example
l | m | sY | H
110.7 GPa | 80.2 GPa | 400 MPa | 100 MPa
11kN
x2
1
5
6
8
7
4
2
x1
3
x3
9
10
11kN
11kN
11kN
12
11
Material properties
Uniaxial stress condition s33 ≠ 0
When Fi = 10 kN, s = 400 MPa (Elastic limit)
Elastoplastic when Fi = 10 ~ 11kN
%
% Two-element example
%
% Nodal coordinates
XYZ=[0 0 0; 1 0 0; 1 1 0; 0 1 0;
0 0 1; 1 0 1; 1 1 1; 0 1 1;
0 0 2; 1 0 2; 1 1 2; 0 1 2]*0.01;
%
% Element connectivity
LE=[1 2 3 4 5 6 7 8;
5 6 7 8 9 10 11 12];
%
% Prescribed displacements [Node, DOF, Value]
SDISPT=[1 1 0;1 2 0;1 3 0;2 2 0;2 3 0;3 3 0;4 1 0;4 3 0];
1
4
3
2
x1
x2
u=v=w=0
v=w=0
w=0
u=w=0

## Slide 57: Tension of Elastoplastic Bar Example
%
% External forces [Node, DOF, Value]
EXTFORCE=[9 3 10.0E3; 10 3 10.0E3; 11 3 10.0E3; 12 3 10.0E3];
%
% Load increments [Start End Increment InitialFactor FinalFactor]
TIMS=[0.0 0.8 0.4 0.0 0.8; 0.8 1.1 0.1 0.8 1.1]';
%
% Material properties PROP=[LAMDA MU BETA H Y0]
MID=1;
PROP=[110.747E9 80.1938E9 0.0 1.E8 4.0E8];
%
% Set program parameters
ITRA=70; ATOL=1.0E5; NTOL=6; TOL=1E-6;
%
% Calling main function
NOUT = fopen('output.txt','w');
NLFEA(ITRA, TOL, ATOL, NTOL, TIMS, NOUT, MID, PROP, EXTFORCE, SDISPT, XYZ, LE);
fclose(NOUT);
0
1.1
0.4
0.9
0.8
1
4
8
9
10
11
Time
Force (kN)
10kN * 1.1 = 11kN

## Slide 58: Tension of Elastoplastic Bar Example
Time Time step Iter Residual
0.40000 4.000e-01 2 3.80851e-12
Time Time step Iter Residual
0.80000 4.000e-01 2 4.32010e-12
Time Time step Iter Residual
0.90000 1.000e-01 2 3.97904e-12
Time Time step Iter Residual
1.00000 1.000e-01 2 3.63798e-12
Time Time step Iter Residual
1.10000 1.000e-01 2 6.66390e+02
3 1.67060e-09
Convergence iteration outputs (output.txt)
Linear elastic region
Elastoplastic region
Load factor | u5z | u9z | S33 Elem1 | S33 Elem2 | State
0.4 | 7.73×10−6 | 1.55×10−5 | 160 MPa | 160 MPa | Elastic
0.8 | 1.55×10−5 | 3.09×10−5 | 320 MPa | 320 MPa | Elastic
0.9 | 1.74×10−5 | 3.48×10−5 | 360 MPa | 360 MPa | Elastic
1.0 | 1.93×10−5 | 3.87×10−5 | 400 MPa | 400 MPa | Elastic
1.1 | 4.02×10−3 | 8.04×10−3 | 440 MPa | 440 MPa | Plastic