## Slide 1: Tutorial 4: 2D Plane (CST/Q4)

## Slide 2: CANTILEVER BEAM
E = 200 GPa, n=0.3
Thickness t = 0.01 m
1m
5m
100 kN-m

## Slide 3: CANTILEVER BEAM (CST)
Parts
  2D Planar, Deformable, Shell, App Size = 10
  Create lines (rectangle): (0, 0), (5, 1)
Materials
  Mechanical, Elasticity, Elastic
  Young’s modulus = 200E9, Poisson’s ratio = 0.3
Sections
  Solid, Homogeneous
  Set plane stress/strain thickness to 0.01 m
Assign the section to the part

## Slide 4: CANTILEVER BEAM (CST)
Assembly, Instance
Steps
  Linear perturbation, Static
BCs
  Initial, Encastre + Displacement/Rotation, U2
Tip
  To change BC symbols: View, Assembly Display Options, Attribute
Encastre
U2

## Slide 5: CANTILEVER BEAM (CST)
Loads
  Mechanical, Pressure, select upward, Uniform, 30
Mesh
  Assign Mesh Controls, Tri (Tri only)
  Global element size = 1
Mesh control
  Edit Mesh, Element, Swap diagonal
100 kN-m
1m
100 kN-m
1m
100 kN-m

## Slide 6: CLAMPED-CLAMPED BEAM (CST)
Analysis, Create Job, Data Check, Submit
Results
Deformed plot, Stress plots
  Field output, Mises, S11, S22, S12
  Field output, U, U2
Plot symbols
  Plot stress direction
  Make sure the “Field output tool box”
S11
S22

## Slide 7: CANTILEVER BEAM (Q4)
The same procedures of Parts to Loads as CST
Mesh
  Assign Mesh Controls, Quad (Quad only)
  Element Type, Quad tap, uncheck “Reduced integration”
  Global element size = 1
Analysis, Create Job, Data Check, Submit
Results
Plot symbols
S11
S22