## Slide 1: Tutorial 5-1: Part Sketch / Geometric Constraints

## Slide 2: A BRACKET ANALYSIS
A bracket with a shaft hole
  E=210 Gpa, Poison ratio 0.3
  Thickness t=0.1 m
0.15
R0.1
R0.05
0.15
0.05
Fillet
R0.02
150kN
100kN
FIXED BC

## Slide 3: PART MODULE (SKETCH)
Sketch
  Draw outlines of the bottom of the bracket
Tip
  Starting and ending point of a circle is recognized as a dividing point
  Case 1
  Case 2
Delete the bottom half
Delete the bottom half
One geometric object
Two geometric objects

## Slide 4: PART MODULE (SKETCH)
Sketch
  Menu/Edit/Auto-Trim, delete half of the outer circle
  Menu/Add/Fillet, add two fillets, radius of those fillets is 0.02
Fillet radius = 0.02
Fillet center point
Add two fillets
Auto trim

## Slide 5: PROPERTY / ASSEMBLY / STEPS MODULES
Materials
  Mechanical, Elasticity, Elastic
  Young’s modulus = 210E9, Poisson’s ratio = 0.3
Sections
  Solid, Homogeneous
  Set plane stress/strain thickness to 0.1 m
Assign the section to the part
Assembly, Instance
Steps
  Linear perturbation, Static

## Slide 6: INTERACTION MODULE (MPC)
How to apply loads at the center of shaft hole?
  Side tool bar/Create a reference point (RP) at the center of the shaft hole
  Menu/Constraint/Create/MPC Constraint MPC (Multiple point constraints)
  Select the RP as the MPC control point (master node)
  Select the circumference of the hole shaft as the slave nodes
  MPC type select as of Beam
Reference Point
Applied Beam type MPCs

## Slide 7: MPC Types
Beam type
  Provide a rigid beam between the master node and slave nodes
  Constraint the “displacement” and “rotation” of the master node to the “displacement” and “rotation” of the slave nodes.
  Distant between the master and slave nodes remain the same
Pin type
  Constraint equal global displacements between the master node and slave nodes
  Constraint the “displacement” of the master node to the “displacement” of the slave nodes.

## Slide 8: LOADS / JOB / VISUALIZATION MODULES
Loads
  Mechanical, Concentrated force, Uniform, CF1 = -200kN CF2 = 150kN
BCs
  Step1, ENCASTRE
Analysis, Create Job, Data Check, Submit
Results
  Max Von Mises 37 MPa
FIXED BC

## Slide 9: A BRACKET DESIGN
A bracket design
  Maximum stress is of 50MPa
  Find optimum size of the outer radius (Rout)
  0.07 m ≤ Rout ≤ 0.1 m
0.15
R0.1
R0.05
0.15
0.05
Fillet
R0.02
150kN
100kN
FIXED BC

## Slide 10: PART MODULE
Modify the current design
  Modify part to modify the current design
Model tree / expand “Parts” / expand your part (default name: “Part-1”) / expand “Features” / expand your sketch (default name: “Shell planar”) / double click “Section Sketch”
Menu/Edit/Dimension
  Set the outer radius dimension to 0.07 as a trial and error process

## Slide 11: GEOMETRIC CONSTRAINTS
What happens?
  Un desirable design perturbation (unsymmetric design)
Proper geometric constraints are needed
  Add dimension from the shaft center and the edge at the bottom left to restrict the model remains symmetric as design parameter (the radius of the outer circle) is perturbed.

## Slide 12: GEOMETRIC CONSTRAINTS
After design perturbation
  Max Von Mises stress increased to 69 Mpa (Violation of the maximum stress constraint)
  Repeat the other trials to find optimum design while satisfying the maximum stress constraint

## Slide 13: Tutorial 5-2: 2D Plane (basic modeling technique)

## Slide 14: PANEL WITH A HOLE
A panel with a hole - E = 200 GPa, n=0.3 - Thickness t = 0.01 m
2m
5m
50 kPa
50 kPa
R=0.25

## Slide 15: PANEL WITH A HOLE
E = 200 GPa, n=0.3
Thickness t = 0.01 m
1m
2.5m
50 kPa
R=0.25
U2=UR1=UR3=0 (YSYMM)
U1=UR2
=UR3=0
(XSYMM)

## Slide 16: PARTS MODULE
Parts
  2D Planar, Deformable, Shell, App Size = 10
  Create lines (rectangle): (0, 0), (2.5, 1)
  Create circle (center and perimeter): (0, 0), (0.25, 0)
  Auto trim
Tip
  Even a circle has a starting point and ending point on circumference

## Slide 17: PROPERTY / ASSEMBLY / STEPS MODULES
Materials
  Mechanical, Elasticity, Elastic
  Young’s modulus = 200E9, Poisson’s ratio = 0.3
Sections
  Solid, Homogeneous
  Set plane stress/strain thickness to 0.01 m
Assign the section to the part
Assembly, Instance
Steps
  Linear perturbation, Static

## Slide 18: LOADS MODULE
BCs
  Step1, Symmetric, XSYMM and YSYMM
Tip
  To change BC symbols: View, Assembly Display Options, Attribute
Loads
  Mechanical, Pressure, Uniform, -50000 (-50 kPa)
U2=UR1=UR3=0 (YSYMM)
U1=UR2
=UR3=0
(XSYMM)

## Slide 19: MESH MODULE (MESHING TECHNIQUE)
Structured mesh
  Follows predefined mesh patterns (Rule based meshing)
  Predictable mesh shape
  Not applicable for every geometry domain (If geometry domain is not affordable for structured mesh, a warning message and reasons will appear)
  For 2D/Quad-dominated mesh, the geometry domain better have 4 edges
Free mesh
  No predefined mesh patterns
  Flexibility
  Impossible to predict a free mesh pattern

## Slide 20: MESH MODULE (PARTITION FACE)
Mesh
  Menu: Tool/Partition/Partition Face/Sketch (sketch mode)
  Draw 3 lines
  Menu/Edit/Auto-trim, delete the red line
  Assign Mesh Controls, Quad (Quad only), Structured
  Global seed, size 0.1
0.5m
0.5m
Auto trim

## Slide 21: MESH MODULE (SEED MESH)
Seed
  Menu: Seed/Edge biased
  Select lines, Bias ratio of 3, # of elements along the edge of 5
Tip
  When you select the edges, pick near the end where the mesh must be denser (red arrow shows mesh density direction)
  Bias ratio: the ratio of size of a starting and ending element
  EX) Bias ratio of 3, # of elements along the edge of 3
a
3a

## Slide 22: MESH / JOB / VISUALIZATION MODULES
Seed
  Menu: Seed/Edge by number
  Select lines, # of elements along the edge of 5
  Mesh part
Analysis, Create Job, Data Check, Submit
Results
Deformed plot, Stress plots
  Field output, Mises