## Slide 1: CHAP 8 STRUCTURAL DESIGN USING FINITE ELEMENTS
FINITE ELEMENT ANALYSIS AND DESIGN
Nam-Ho Kim

## Slide 2: INTRODUCTION
FEA: determining the response of a given structure for a given set of loads and boundary conditions
  Geometry, material properties, BCs and loads are well defined
Engineering design: a process of synthesis in which parts are put together to build a structure that will perform a given set of functions satisfactorily
Analysis is systematic and can be taught easily; design is an iterative process
Creative design: creating a new structure or machine that does not exist
Adaptive design: modifying an existing design (evolutionary process)

## Slide 3: INTRODUCTION – STRUCTURAL DESIGN
Structural design: a procedure to improve or enhance the performance of a structure by changing its parameters
Performance: a measurable quantity (constraint and goal)
  the weight, stiffness or compliance; the fatigue life; noise and vibration levels; safety
Constraint: As long as the performance satisfies the criterion, its level is not important
  Ex: the maximum stress should be less than the allowable stress
Goal: the performance that the engineer wants to improve as much as possible
Design variables: system parameters that can be changed during the design process
  Plate thickness, cross-sectional area, shape, etc

## Slide 4: SAFETY MARGIN
Factor of Safety (stress performance)
  Structures should satisfy a constraint:
  si(x): the calculated stress at a point x in the i-th component
  sallowable: allowable stress from material strength (failure strength)
  Factor of safety: effect of material variability, experimental errors, etc
For general type of performance, use response and capacity
  Response Ri: calculated value of performance
  Capacity Ci: allowed value of performance
  When multiple loads are applied simultaneously

## Slide 5: SAFETY MARGIN cont.
Safety Margin: the excess capacity compared with the response
  The member can afford additional Zi stress before it fails
Sufficiency Factor Si: ratio of the allowable capacity to the response
  Normalized in terms of the capacity

## Slide 6: LOAD FACTOR
Instead of dividing the capacity by SF, increase applied loads
Load factor l: the factor by which the applied loads must be multiplied just enough to cause the structure to fail
Let a set of loads be F = {F1, F2, …, FN}T. For a given failure strength Ci, the load factor is defined by
For proportional loading with linear system
Load factor is the ratio between capacity and response
The structure should be designed in order to satisfy a given level of load factor

## Slide 7: EXAMPLE
Design the height h of cantilevered beam with SF = 1.5
  E = 2.9104 ksi, w = 2.25 in.
Allowable tip deflection Dallowable = 2.5 in. (No need SF)
  FE equation after applying BCs
  FE solution
F = 2,000 lb
L = 100 in
h
w

## Slide 8: EXAMPLE cont.
Failure strength = 40 ksi (Need SF)
  Supporting moment at the wall
  Maximum stress at the wall
  Height calculation with the factor of safety

## Slide 9: FULLY-STRESSED DESIGN
For complex structure with different failure criteria needs an iterative process to find the best design – Intuitive design
Fully-Stressed Design: Very useful with stress and minimum gage constraints
  From the observation that all members will be in the allowable stress level unless they reach the minimum gage
  It is based on an assumption that the effect of adding or removing material from a member is to change the stresses in that member
  Works well with statically determinate structure (member force does not change when the cross-section increases)
For the best design, each member of the structure that is not at its minimum gage is fully stressed under at least one of the design load conditions

## Slide 10: FSD cont.
Assume the loads carried by members remained constant
Stress in each member is calculated
Member is resized to bring the stress to the allowable value
Truss example (member force F = s·A)
If member forces are constant (statically determinant system), one iteration to come up FSD
Repeated calculations are required when member forces vary
If Anew is less than the minimum gage, choose min. gage

## Slide 11: FSD cont.
Beam element: Use section modulus
  Maximum bending stress
  Update section modulus
  If M remains constant, one iteration yields FSD
The section modulus in beam corresponds to cross-sectional area in truss
Section modulus

## Slide 12: FSD EXAMPLE – CANTILEVERED BEAM
Initial w = 2.25, h = 3.5 in. Determine new height using FSD
Section modulus and max. stress at the initial design
New section modulus using stress ratio resizing
F = 2,000 lb
L = 100 in
h
w
Only one iteration for FSD

## Slide 13: DESIGN PARAMETERS
Selecting design variables – easy for beam and truss, but more complicated for plane or 3D solids
Material property design variable
  Varying material properties to find the best material
  Not common, but useful for designing composite materials
Sizing design variable
  Geometric parameters as design (parametric design variable)
  Appears as a parameter in FEM
  Thickness of plate/shell, cross-sectional geometry of truss/beam, etc
r
b
h
t
r
t
w
h
b
b
h
t
w

## Slide 14: DESIGN PARAMETERS cont.
Shape design variable
  Related to the structure’s geometry, which does not appear explicitly as a parameter
  Beam cross-section is a geometry, but it appears as a moment of inertia
  Cx, Cy, and r determine the size and location of the hole
  Shape design variables change FE mesh
  Design variables must be limited so that the hole remains inside of the plate
Cx
Cy
Cx
Cy
r
r
(a) Initial design
(b) Perturbed design

## Slide 15: DESIGN PARAMETERS cont.
Shape design variable cont.
  Shape design variable describe the movement of boundary
  Mesh inside of structure must move accordingly
Iso-parametric mapping method
  Works well with mapped mesh, maintaining topological mesh
  Convenient on tracking the same elements and nodes
  Possible mesh distortion for large shape-changing design
(a) Initial mesh
(b) Perturbed mesh
r
r

## Slide 16: PARAMETER STUDY – SENSITIVITY ANALYSIS
Parameter study
  Effect of a design variable on performance (gradual change of DV)
  Cantilevered beam example:
Allowable stress
Acceptable region
w (in) | h (in) | smax (ksi)
2.0 | 4.0 | 37.5
2.0 | 4.5 | 29.6
2.0 | 5.0 | 24.0
2.5 | 4.0 | 30.0
2.5 | 4.5 | 23.7
2.5 | 5.0 | 19.2
3.0 | 4.0 | 25.0
3.0 | 4.5 | 19.8
3.0 | 5.0 | 16.0

## Slide 17: SENSITIVITY ANALYSIS
Parameter study becomes too expensive with many DVs
Unable to capture rapid change in performance locally
Design sensitivity analysis computes the rate of performance change with respect to design variables
Sensitivity analysis calculates gradient of performance for optimization
Explicit dependence
  Analytical relationship exists between performance and DVs
  Weight of circular cross-section beam
  Sensitivity w.r.t. r:

## Slide 18: SENSITIVITY ANALYSIS cont.
Implicit dependence
  Performance depends on DVs through state variable (displacement)
  Sensitivity of stress:
How to calculate displacement sensitivity?
  Differentiate finite element equation:
  [dK/db] and {dF/db} can be evaluated using either their analytical expression or numerical differentiation
Easy to calculate from given expression of stress
Difficult to calculate, time consuming

## Slide 19: SENSITIVITY ANALYSIS cont.
Sensitivity equation must be solved for each design variable
Sensitivity equation uses the same stiffness matrix with the original finite element analysis
Consider RHS as a pseudo-force vector
Similar to finite element analysis with multiple load cases
Thus, solving sensitivity equation is very inexpensive using factorized stiffness matrix
General form of performance
  Sensitivity
Explicit dependent term
Implicit dependent term

## Slide 20: FINITE DIFFERENCE SENSITIVITY
Easiest way to compute sensitivity information of the performance
Calculate performance at two different designs
Forward difference method
Central difference method
Consider FEA as a black-box
Sensitivity computation cost becomes high for many design variables
  n+1 analyses for forward FDM
  2N+1 analyses for central FDM

## Slide 21: FINITE DIFFERENCE SENSITIVITY cont.
Accuracy of finite difference sensitivity
  Accurate results can be expected when Db approaches zero
  For nonlinear performances, a large perturbation yields completely inaccurate results
  Numerical noise becomes dominant for a too-small perturbation size
H
b0
b1
b2
b3
b4
b
(dH/db)4
(dH/db)3
(dH/db)2
(dH/db)1

## Slide 22: EXAMPLE – CANTILEVERED BEAM
At optimum design (w=2.25 in, h=4.47 in), calculate sensitivity of tip displacement w.r.t. h
Exact sensitivity:
Differentiate [K]
Pseudo load vector

## Slide 23: EXAMPLE – CANTILEVERED BEAM cont.
Sensitivity equation:
Same way of applying BC
Sensitivity of nodal DOFs
  Same with the exact sensitivity

## Slide 24: STRUCTURAL OPTIMIZATION
What Is Design Optimization?
  To find the best design parameters that meet the design goal and satisfies constraints.
Design Parameters: Anything the Designer Can Change
  Thickness of a plate
  Cross-sectional geometry of a beam or truss
  Geometric dimensions
Design Goal: Objective Function
  Design criterion that will be minimized (or maximized)
  Mass, Stress, Displacement, Natural Frequency, ETC
Constraint: Conditions that the system must satisfy
  Stress, Displacement, ETC
Note: Design parameters must affect the design goal and constraints.

## Slide 25: OPTIMIZATION FLOW CHART
Yes
No
Physical engineering problem
Structural modeling
Design parameterization
Performance definition (cost, constraints)
Structural analysis (FEM, BEM, CFD…)
Design sensitivity analysis
Structural model update
Optimized?
Stop

## Slide 26: THREE-STEP PROBLEM FORMULATION
Design Parameterization
  Clear identification
  Independence of designs
Objective Function
  Must be a function of design parameters
  Minimization ( –Maximization)
Constraint Functions
  Inequality constraints
  Equality constraints
  Equality constraints must be less than the number of design parameters
h
w
t2
t1

## Slide 27: STANDARD FORM
Standard form of design optimization
Feasible set: the set of designs that satisfy constraints

## Slide 28: BEER CAN EXAMPLE
Design the beer can size so that the minimum amount of sheet metal can be used (minimize manufacturing cost)
Constraints
  It is required to hold at least 400 ml of fluid.
  The diameter of the can should be no more than 8 cm. In addition, it should not be less than 3.5 cm (shipping & handling).
  The height of the can should be no more than 18 cm and no less than 8 cm.
D
H

## Slide 29: BEER CAN EXAMPLE cont.
Standard Form
Feasible Domain
S

## Slide 30: GLOBAL OPTIMIZATION
Global Optimum
  A point b* is called a global minimum for f(b) if
There is no mathematical method to find the global minimum
Weierstrass theorem: Existence of global minimum
  If f(b) is continuous and the set S is closed and bounded, then there is a global minimum
Local Optimum
  A point b* is called a local minimum for f(b) if
  for all bS in a small neighborhood of b*
Global optimum: b3
Local optima: b1, b3, b5
Feasible set
b1
b3
b5
b2
b4
b6
b
f(b)

## Slide 31: GRAPHICAL OPTIMIZATION
Graphical methods can be used to solve the optimization problem when it has only one or two design variables
Graphical methods are expensive but help to visualize the design space and to understand the nature of design problem
Draw the design space (lower- & upper-bounds of DVs)
Plot constraints on the graph (feasible set)
Plot contour lines of objective function
Find the optimum point (the objective function has the lowest value within the feasible set)

## Slide 32: EXAMPLE – BEER CAN OPTIMIZATION

## Slide 33: NUMERICAL METHODS
In FEA, we don’t know the explicit relationship, f(b), between design parameters and objective (or constraint) function.
But, we can calculate f(b) for a given b by solving the finite element equation.
Then, how can we find the optimum design?
Use Numerical Method
Numerical Method
  From the current design, find the next design that can reduce the objective function and satisfy constraints.
  Repeat the search until there is no way to improve the objective function further.

## Slide 34: NUMERICAL METHOD cont.
Basic Algorithm
  Start with b(K) and K = 0.
    Initial design must be given
  Evaluate function values and their gradients.
    Using finite element analysis
  Using information from Step 2, determine ∆b(K).
    Design change
  Check for termination.
    Stop if the problem is converged.
  Update design
  Increase K = K + 1 and go to Step 2.
    Design iteration (cycle)

## Slide 35: NUMERICAL METHOD cont.
Change in Design
  αK: Step size
  d(K): Search direction vector
  Design change means the determination of search direction and step size.

## Slide 36: OPTIMIZATION USING EXCEL SOLVER
Four-bar truss optimization
2F
L
L
F
1
2
3
4
1
2
3
4