## Slide 1: CHAP 5 FINITE ELEMENTS FOR HEAT TRANSFER PROBLEMS
FINITE ELEMENT ANALYSIS AND DESIGN
Nam-Ho Kim

## Slide 2: HEAT CONDUCTION ANALYSIS
Analogy between Stress and Heat Conduction Analysis
  In finite element viewpoint, two problems are identical if a proper interpretation is given.
More Complex Problems
  Coupled structural-thermal problems (thermal strain).
  Radiation problem
Structural problem | Heat transfer problem
Displacement | Temperature (scalar)
Stress/strain | Heat flux (vector)
Displacement B.C. | Fixed temperature B.C.
Surface traction force | Heat flux B.C.
Body force | Internal heat generation
Young’s modulus | Thermal conductivity

## Slide 3: THERMAL PROBLEM
Goals:
  Solve for temperature distribution for a given thermal load.
Boundary Conditions
  Essential BC: Specified temperature
  Natural BC: Specified heat flux

## Slide 4: STEADY-STATE HEAT TRANSFER PROBLEM
Fourier Heat Conduction Equation:
  Heat flow from high temperature to low temperature
Examples of 1D heat conduction problems
Thermal conductivity (W/m/C )
Heat flux (Watts)
Thigh
qx
Tlow
qx
Thigh
Tlow

## Slide 5: GOVERNING DIFFERENTIAL EQUATION
Conservation of Energy
  Energy In + Energy Generated = Energy Out + Energy Increase
Two modes of heat transfer through the boundary
  Prescribed surface heat flow Qs per unit area
  Convective heat transfer
  h: convection coefficient (W/m2/C )
Qg
Qs
A
dx

## Slide 6: GOVERNING DIFFERENTIAL EQUATION cont.
Conservation of Energy at Steady State
  No change in internal energy (DU = 0)
  P: perimeter of the cross-section
Apply Fourier Law
  Rate of change of heat flux is equal to the sum of heat generated and heat transferred

## Slide 7: GOVERNING DIFFERENTIAL EQUATION cont.
Boundary conditions
  Temperature at the boundary is prescribed (essential BC)
  Heat flux is prescribed (natural BC)
  Example: essential BC at x = 0, and natural BC at x = L:

## Slide 8: DIRECT METHOD
Follow the same procedure with 1D bar element
  No need to use differential equation
Element conduction equation
  Heat can enter the system only through the nodes
  Qi: heat enters at node i (Watts)
  Divide the solid into a number of elements
  Each element has two nodes and two DOFs (Ti and Tj)
  For each element, heat entering the element is positive
Ti
e
Tj
j
i
1
2
N
Q1
Q2
QN
Q3
L(e)
xi
xj

## Slide 9: ELEMENT EQUATION
Fourier law of heat conduction
From the conservation of energy for the element
Combine the two equation
  Similar to 1D bar element (k = E, T = u, q = f)
Element conductance matrix

## Slide 10: ASSEMBLY
Assembly using heat conservation at nodes
  Remember that heat flow into the element is positive
  Equilibrium of heat flow:
  Same assembly procedure with 1D bar elements
Applying BC
  Striking-the-rows works, but not striking-the-columns because prescribed temperatures are not usually zero
Element 1
Q2
2
Element 2
1
3

## Slide 11: EXAMPLE
Calculate nodal temperatures of four elements
  A = 1m2, L = 1m, k = 10W/m/C
Element conduction equation
200 C
x
T1
T2
T3
T4
T5
1
2
3
4
Q4 = –200W
Q5 = 0
Q3 = 0
Q1
Q2 = 500W

## Slide 12: EXAMPLE cont.
Assembly
Boundary conditions (T1 = 200 oC, Q1 is unknown)

## Slide 13: EXAMPLE cont.
Boundary conditions
  Strike the first row
  Instead of striking the first column, multiply the first column with T1 = 200 oC and move to RHS
  Now, the global matrix is positive-definite and can be solved for nodal temperatures

## Slide 14: EXAMPLE cont.
Nodal temperatures
How much heat input is required to maintain T1 = 200oC?
  Use the deleted first row with known nodal temperatures
Other example
50 C
x
200W
Q = 0
1
100W
Q = 0
2
3
4
5
1
3
4
2
5

## Slide 15: GALERKIN METHOD FOR HEAT CONDUCTION
Direct method is limited for nodal heat input
Need more advanced method for heat generation and convection heat transfer
Galerkin method in Chapter 3 can be used for this purpose
Consider element (e)
Interpolation
Heat flux
Ti
e
Tj
j
i
L(e)
xi
xj
Temperature varies linearly
Heat flow is constant

## Slide 16: GALERKIN METHOD cont.
Differential equation with heat generation
Substitute approximate solution
Integrate the residual with Ni(x) as a weight
Integrate by parts
Residual

## Slide 17: GALERKIN METHOD cont.
Substitute interpolation relation
Perform integration
Repeat with Nj(x) as a weight

## Slide 18: GALERKIN METHOD cont.
Combine the two equations
  {Q(e)}: thermal load corresponding to the heat source
  {q(e)}: vector of nodal heat flows across the cross-section
Uniform heat source
  Equally divided to the two nodes
Temperature varies linearly in the element, and the heat flux is constant
Similar to 1D bar element

## Slide 19: EXAMPLE
Heat chamber
Wall temperature = 200 C
Uniform heat source inside the wall Q = 400 W/m3.
Thermal conductivity of the wall is k = 25 W/mC.
Use four elements through the thickness (unit area)
Boundary Condition:
T1 = 200, qx=1 = 0.

## Slide 20: EXAMPLE cont.
Element Matrix Equation
  All elements are identical
  Assembly

## Slide 21: EXAMPLE cont.
Boundary Conditions
  At node 1, the temperature is given (T1 = 200). Thus, the heat flux at node 1 (Q1) should be unknown.
  At node 5, the insulation condition required that the heat flux (Q5) should be zero. Thus, the temperature at node 5 should be unknown.
  At nodes 2 – 4, the temperature is unknown (T2, T3, T4). Thus the heat flux should be known.
1
2
3
4
5
Q1
Q5

## Slide 22: EXAMPLE cont.
Imposing Boundary Conditions
  Remove first row because it contains unknown Q1.
  Cannot remove first column because T1 is not zero.
  Instead, move the first column to the right.

## Slide 23: EXAMPLE cont.
Solution
Discussion
  In order to maintain 200 degree at node 1, we need to remove heat

## Slide 24: CONVECTION BC
Convection Boundary Condition
  Happens when a structure is surrounded by fluid
  Does not exist in structural problems
  BC includes unknown temperature (mixed BC)
  Heat flow is not prescribed. Rather, it is a function of temperature on the boundary, which is unknown
1D Finite Element
  When both Nodes 1 and 2 are convection boundary
Wall
T
T
qh
T1
T2
Fluid Temperature
Convection Coefficient

## Slide 25: EXAMPLE (CONVECTION ON THE BOUNDARY)
Element equation
Balance of heat flow
  Node 1:
  Node 2:
  Node 3:
Global matrix equation
T1
T2
T3
1
2
h3
h1

## Slide 26: EXAMPLE cont.
Move unknown nodal temperatures to LHS
The above matrix is P.D. because of additional positive terms in diagonal
How much heat flow through convection boundary?
  After solving for nodal temperature, use
This is convection at the end of an element

## Slide 27: EXAMPLE: FURNACE WALL
Firebrick k1=1.2W/m/oC hi=12W/m2/oC
Insulating brick k2=0.2W/m/oC ho=2.0W/m2/oC
Firebrick
Tf = 1,500 C
0.25 m
x
Insulating brick
Ta = 20 C
0.12 m
ho
hi
No heat flow
1,500 C
x
T1
T2
T3
Tf
Ta
1
2
ho
hi
20 C
Convection boundary
Convection boundary

## Slide 28: CONVECTION ALONG A ROD
Long rod is submerged into a fluid
Convection occurs across the entire surface
Governing differential equation
Convection
Convection
h
b
Fluid T 
i
j
xi
xj

## Slide 29: CONVECTION ALONG A ROD cont.
DE with approximate temperature
Minimize the residual with interpolation function Ni(x)
Integration by parts

## Slide 30: CONVECTION ALONG A ROD cont.
Substitute interpolation scheme and rearrange
Perform integration and simplify
Repeat the same procedure with interpolation function Nj(x)

## Slide 31: CONVECTION ALONG A ROD cont.
Finite element equation with convection along the rod
Equivalent conductance matrix due to convection
Thermal load vector

## Slide 32: EXAMPLE: HEAT FLOW IN A COOLING FIN
k = 0.2 W/mm/C, h = 2104 W/mm2/C
Element conductance matrix
Thermal load vector
Element 1
Convection
330 C
T  = 30 C
120 mm
160 mm
1.25 mm
T1
T2
T3
T4
x
Insulated
1
2
3

## Slide 33: EXAMPLE: HEAT FLOW IN A COOLING FIN cont.
Element conduction equation
  Element 1
  Element 2
  Element 3
Balance of heat flow
  Node 1
  Node 2
  Node 3
  Node 4

## Slide 34: EXAMPLE: HEAT FLOW IN A COOLING FIN cont.
Assembly
Move T4 to LHS and apply known T1 = 330
Move the first column to RHS after multiplying with T1=330

## Slide 35: EXAMPLE: HEAT FLOW IN A COOLING FIN cont.
Solve for temperature